## Slide 1
RB7300T PJT
TRAINING MANUAL
SAMSUNG Bottom Mounted Freezer Refrigerator
BOTTOM MOUNTED FREEZER TYPE
BASIC MODEL : RL38T775CSR/EG
MODEL CODE : RB38T* / RB36T* / RB34T*
RL38T* / RL36T* / RL34T*
RB38A* / RB34A*
RL38A* / RL34A*
RB38B* / RB33B*
2021

## Slide 2
IMPORTANT SAFETY NOTICE
2
The service guide is for professional repairers who have technical competence to repair refrigerating appliances and comply with all applicable regulations for repairers of electrical equipment
Any attempt to repair the appliance by a non-professional repairer may result in personal injury and property damage.
The manufacturer or dealer will not be held responsible for the interpretation of this information.
All rights reserved. This service guide may not be reproduced in whole or as a part in any form whatsoever without the written permission of the SAMSUNG ELECTRONICS Company
Samsung is not liable for any damage to product, any injury or any other product safety issue caused by any attempt to repair the product which does not carefully follow these repair and maintenance instructions or carried out by a non-authorized service provider, self-repair or non-professional repair of the product, Any damage to the product caused by an attempt to repair the product by any person other than a Samsung authorises service provider will not be covered by the warranty.
For information about purchasing parts and tools, please visit http://samsung.com/support

## Slide 3
Contents
1
Precautions(Safety Warnings)---- 9
2
Product Specifications------------- 14
2-1) Introduction of Main Function...................................................14
2-2) Model Specification ...................................................................21
2-3) Electric Parts Specification.......................................................28
2-4) Dimensions of Refrigerator....................................................... 30
2-5) Refrigerant Route in Refrigeration cycle................................ 32
2-6) Principle Of Freezer................................................................... 34
2-7) Operation theory of refrigeration cycle components............ 37
2-8) Interior Views............................................................................. 41
3
3
Functions & Features---------------- 42
3-1) Control Display......................................................................... 42
3-2) Knob Control..............................................................................44

## Slide 4
Contents
4
Disassembly & Reassembly------- 45
4
4-1) Precaution.................................................................................................45
4-2) Assy PCB...................................................................................................48
4-3) Assy Top Table.........................................................................................50
4-4) Reed Switch...............................................................................................52
4-5) Temp Sensor..............................................................................................53
4-6) Buzzer.........................................................................................................54
4-7) Wi-fi Module................................................................................................55
4-8) Hinge Upp...................................................................................................56
4-9) Refrigerator Door.......................................................................................57
4-10) Hinge Mid.................................................................................................58
4-11) Reed Switch (Non Bespoke)..................................................................59
4-11) Reed Switch (Bespoke)..........................................................................60
4-12) Freezer Door............................................................................................61
4-13) Bespoke Panel Door (Ref)......................................................................62
4-14) Bespoke Panel Door(Fre).......................................................................63
4-15) Door Gasket.............................................................................................64
4-16) Door Handle (Bar)...................................................................................65
4-17) Assy Case Veg Up...................................................................................66
4-18) Case Veg Low..........................................................................................67
4-19) Tray Freezer.............................................................................................68
4-20) Shelf Ref...................................................................................................69
4-21) Wine Rack................................................................................................70
4-22) Shelf Veg Up............................................................................................71
4-23) Shelf Veg Low........................................................................................72
4-24) Cover Evap Ref (Twin Cooling)............................................................73

## Slide 5
Contents
4
Disassembly & Reassembly------- 45
5
4-25) Sensor temp-Ref (Twin Cooling)..............................................................74
4-26) Motor Fan-Ref (Twin Cooling)...................................................................75
4-27) Cover Multi Ref (Mono Cooling)................................................................76
4-27) Cover Multi Ref (RB33A*)...........................................................................77
4-28) Sensor temp (Mono Cooling).....................................................................78
4-29) Damper (Mono Cooling)..............................................................................79
4-30) Knob (RB33A*).............................................................................................80
4-31) Cover Evap Freezer......................................................................................81
4-32) Motor Fan.......................................................................................................82
4-33) Sensor temp Fre...........................................................................................83
4-34) Evap Ref (Sensor Temp)..............................................................................84
4-35) Evap Fre (Sensor Temp)..............................................................................85
4-36) LED Lamp......................................................................................................86
4-37) Water Dispenser...........................................................................................89
4-38) Water Tank....................................................................................................90
4-39) Cover Control (Door)...................................................................................91
4-40) Cover Control (Liner)...................................................................................92
4-41) Motor Fan (Machine Compartment)...........................................................93
4-42) Compressor..................................................................................................94
4-43) Relay O/L.......................................................................................................95
4-44) Reversing the Door swing...........................................................................96

## Slide 6
Contents
6
5
Self Diagnosis & Trouble Shooting 110
5-1) Check-List before Trouble-Shooting...............................................................110
5-1-1. Test Function (Forced Operation / Forced Defrost)....................................110
5-1-2. Self-Diagnosis Function..................................................................................116
5-1-3. Load Status Display Function.........................................................................130
5-1-4. Restoration of Previous Settings upon Instant Power Outage...................133
5-1-5. Demo Mode Function for Store Display.........................................................134
5-1-6. Option Setting Function...................................................................................135
5-1-7. Option Table......................................................................................................139
5-2) Troubleshooting Flow-Chart by Symptoms.....................................................143
5-2-1. When Self-Diagnosis Error occurs.................................................................147
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor) (Twin / Bespoke Mono C,D).......167
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor) (Mono C,D,E,F / Bespoke Mono E,F)…….169
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan) (Twin / Bespoke Mono C,D)......171
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan) (Mono C,D,E,F / Bespoke Mono E,F)…….173
5-2-4. When Defrost does not work (F DEF Heater) (Twin / Bespoke Mono C,D).................175
5-2-4. When Defrost does not work (F DEF Heater) (Mono C,D,E,F / Bespoke Mono E,F)........178
5-2-5. When there is No Power (Twin / Bespoke Mono C,D)...................................................181
5-2-5. When there is No Power (Mono C,D,E,F / Bespoke Mono E,F)....................................183
5-2-6. When the Compressor is not working (Twin / Bespoke Mono C,D)............................185
5-2-6. When the Compressor is not working (Mono C,D,E,F / Bespoke Mono E,F).............187
5-2-7. When the unit keeps alarming (Buzzer Sound).............................................................189
5-2-8. When PANEL PCB operates abnormally........................................................................194

## Slide 7
Contents
7
6
PCB Diagram ---------------------------206
6-1) Part Layout (Twin / Bespoke Mono C,D)..............................................................206
6-1) Part Layout (Mono C,D,E,F / Bespoke Mono E,F)................................................207
6-2) Connector Layout & Description (Twin / Bespoke Mono C,D)..........................208
6-2) Connector Layout & Description (Mono C,D,E,F / Bespoke Mono E,F)...........209
6-3) Connector Layout & Description (Wi-Fi Module)................................................210
5-2-9. When the Room Lamp (LED) does not light up (Twin / Bespoke Mono C,D).......196
5-2-9. When the Room Lamp (LED) does not light up (Mono C,D,E,F / Bespoke Mono E,F)...198
5-2-10. When Fridge Damper does not work (Twin / Bespoke Mono C,D).....200
5-2-10. When Fridge Damper does not work (Mono C,D,E,F / Bespoke Mono E,F)........202
5-2-11. When the Wi-Fi does not work properly.........................................204
5
Self Diagnosis & Trouble Shooting 110

## Slide 8
Contents
9
Reference Information -------------215
9-1. Nomenclature ---------------------------------------------------------------------------------- 215
9-2. Trouble Shooting ----------------------------------------------------------------------------- 217
9-3. Q&A ----------------------------------------------------------------------------------------------- 220
8
8
Block Diagram ------------------------ 213
8-1) PBA Main (Twin / Bespoke Mono C,D)...................................................213
8-1) PBA Main (Mono C,D,E,F / Bespoke Mono E,F).....................................214
7
Wiring Diagram -----------------------211
7-1) Wiring Diagram (Twin / Bespoke Mono C,D)...............................................211
7-2) Wiring Diagram (Bespoke Mono E,F/ Mono C,D,E,F)..................................212

## Slide 9
Read all instructions before repairing the product and follow the instructions in order to prevent danger or property damage. Plug out and remove all the items in regrigerator prior to repair.
CAUTION/WARNING SYMBOLS DISPLAYED
Warning
Indicates that a danger of death or serious injury exists.
Caution
Indicates that a risk of personal injury or material damage exists.
means “Prohibited”.
means “Do not disassemble”.
means “No contact”.
means ”Warning or Caution”.
means “Unplug the unit before preforming service”
means “Earth or Ground”.
1. Product Information
9

## Slide 10
Use only correctly rated replacement components and parts.
Check the correct model, rated voltage, rated current, operating temperature etc.
Upon repair, make sure that all harnesses are watertight and are secured.
Secure harnesses tightly in positon to prevent damage and the ingress of moisture or water.
Upon repair, completely remove any dust or other foreign substances from housing, harness, connector, etc.
Cleaning will prevent possible risk of fire or malfunction.
To do list
1. Product Information
10
Rated
components
After repair, Ensure the product is fully reassembled.
It should be returned to the the previous state, with all parts and covers correctly secured in position.

## Slide 11
Check for any water ingress or moisture.
If there is any water or moisture present, take necessary measures such as replacing components, insulation, seals, etc.
Advise users not to put bottles or glass in the freezer.
Advise users not to store tall and narrow bottles or food itmes in the door shelves.
Items may fall out when opening the door causing injury.
To do list
Freezing of the contents may cause the item to explode.
1. Product Information
Advice users not to store items on top of the product.
Opening or closing the door may cause items to fall down causing injury.

## Slide 12
Do not allow users to store pharmaceutical products, scientific materials, etc., in the refrigerator.
Advise users not to attempt tp disassemble, repair or alter the product.
To avoid the risk of fire or product malfunction.
Advise users not to bend the power cord with excessive force and ensure it is not restricted or trapped by heavy items.
To avoid the risk of fire.
Advise users not to plug several appliances into the same socket outlet and not to use extension cables.
To avoid the risk of fire or product malfunction.
To do list
The products which need precise temperature control should not be stored in the refrigerator.
1. Product Information
Prohibited

## Slide 13
Advise users not to install the refrigerator in the wet place or damp areas.
To avoid the risk of fire and electric shock.
Make sure of the earth.
Be sure the product is properly grounded.
To do list
1. Product Information

## Slide 14
Image | Feature
 | SpaceMax Technology (Large Capacity) Store more food with an extra large fridge that holds up to 385 liters* in a standard cabinet depth of 600mm. Its unique SpaceMax™ technology enables the walls to be much thinner as it uses a minimal amount of high-efficiency insulation.
 | All-Around Cooling All-Around Cooling ensures that every item on every shelf and in every box remains evenly chilled. Strategically placed vents circulate cool air everywhere inside the fridge and the freezer to maintain an even and constant temperature that helps foods stay fresh longer.
 | Metal Cooling Metal Cooling plate in the rear wall helps to maintain the optimal internal temperature, longer than a conventional refrigerator without metal cooling. The metal retains the cold from the air, so it prevents the loss of cool air when the door is opened. And its good thermal conductivity helps to quickly restore any heat loss when the door is shut again, so foods are preserved better.
■ A newly developed SAMSUNG BMF refrigerator in 2020 has the following characteristics.
2-1. Introduction of Main Function
To do list
2. Product Specifications

## Slide 15
To do list
2. Product Specifications
2-1. Introduction of Main Function
Image | Feature
 | No Frost Preserve the freshness of food for longer without freezing. No Frost technology maintains a constant optimal temperature in every corner by enhancing the air circulation. It stops the build up of ice on food, like vegetables, so they stay tasting fresh. And avoids the need to defrost your fridge.
 | Optimal Fresh + The Optimal Fresh + box can be used as one drawer or split into two zones to store different types of food using two temperature settings. The left side is cooler and ideal for preserving the natural taste and moisture of meat and fish.
 | Humidity Fresh + Preserve the original texture, flavor and taste of perishable food for longer. Air tight sealing cover at the top of the box protects against moisture loss through strong sealing. Also you can adjust the humidity in the Humidity Fresh + drawer simply by spinning the control dial.
■ A newly developed SAMSUNG BMF refrigerator in 2020 has the following characteristics.

## Slide 16
To do list
2. Product Specifications
2-1. Introduction of Main Function
■ A newly developed SAMSUNG BMF refrigerator in 2020 has the following characteristics.
Image | Feature
 | Power Cool / Power Freeze Delivers a rapid cooling performance to chill beverages and create ice. At the touch of a button, Power Cool blows intensely cold air into the fridge, so food and drinks are quickly chilled. Power Freeze is great for freezing or firming up frozen food, like ice cream, and making more ice.
 | Seamless & Sleek Design RB7300T refrigerator features sleek fit with flat door and recessed handle. The look and feel of the fridge reflects an emerging design trend in kitchens today : clutter-free, simple and clean cabinetry styles, and their accompanying appliances.
 | Clean Back The Clean Back is a completely smooth safety cover for vital coils and cables. It looks really neat, can be easily wiped clean and provides added durability. It stops dirt from collecting around components and protects them from accidental bumps and knocks.

## Slide 17
To do list
2. Product Specifications
2-1. Introduction of Main Function
■ A newly developed SAMSUNG BMF refrigerator in 2020 has the following characteristics.
Image | Feature
 | High Energy Efficiency (Digital Inverter Compressor) Samsung Digital Inverter Compressor smartly controls its speed to deliver only as much cooling as needed whereas the conventional compressor always runs at its maximum level. This variable speed control can significantly enhance the compressor lifetime with perfect performance and that is how Samsung can proudly guarantee 10 year warranty on our compressor.
 | Low Noise 35dB RB7300T decreases averagely 2dB compared to the conventional models thanks to new inverter compressor with New control technology and new high damping rubber damper.
 | Rack & Shelf The wider space of Rack & Shelf makes it easier to store not only standard-sized wines but also thicker champagne bottles. The flattened shelf can hold not only wine but also pizza boxes and egg boxes, making it more versatile.
-2
dB
35dB

## Slide 18
To do list
2. Product Specifications
2-1. Introduction of Main Function
■ A newly developed SAMSUNG BMF refrigerator in 2020 has the following characteristics.
Image | Feature
 | Slide & Fold Shelf Store large and bulky items much more effectively and minimize wasted fridge space. 2 Step Foldable Shelf slides in and out so you can store tall bottles and containers. And it can be easily folded in half to create room for big and bulky items, like a multi-tiered cake or a tower cooker.
 | Easy Door Reversible Generally it is difficult to change the refrigerator door. It needs to be laid down or tilted because the bolts (or some other parts) on the bottom of the fridge must be replaced to reverse door hinge. However all hinges of RB7300T do not need to be laid down for replacement.
 | BPA Free Water Tank Bin Eco-friendly water tank without detection of environmental hormone Bisphenol A.
Lower Hinge
Upper Hinge

## Slide 19
To do list
2. Product Specifications
2-1. Introduction of Main Function
■ A newly developed SAMSUNG BMF refrigerator in 2021 has the following characteristics.
Image | Feature
 | BESPOKE – Customizable Design Create a beautifully stylish and unique kitchen space that really stands out. The refrigerator has a customizable design, so you can choose a finish that will blend harmoniously with your kitchen furniture and fittings. It is available in a choice of 6 materials: Satin Glass, Glam Glass, Clean Glass, Cotta Metal, Real Stainless and Steel Metal. And you can combine these with various stylish door colors options to suit your kitchen design and personal taste.
 | BESPOKE – Customizable Inner Space Upgrade your refrigerator to suit your lifestyle with a customizable inner space. A multi-functional Rack & Shelf™ with a wider and flatter shape holds thicker wine bottles or food like pizza. And a 2 Step Foldable Shelf slides in and out and folds in half to store tall bottles and bulky items.
 | Twin Cooling Plus™ Ensure that your food stays moister and fresher for longer*. Twin Cooling Plus™ quickly optimizes the temperature and humidity in the fridge and freezer with independent cooling. It preserves food in the best conditions and protects its natural flavor and aroma by preventing odors from mixing.

## Slide 20
To do list
2. Product Specifications
2-1. Introduction of Main Function
■ A newly developed SAMSUNG BMF refrigerator in 2021 has the following characteristics.
Image | Feature
 | CoolSelect Plus Enjoy the ultimate in flexible storage using the CoolSelect Plus zone. With one touch it can switch modes to store different foods at the optimum temperature, so that everything stays fresher. Simply select Cool (2℃), Chill (-1℃), Soft Freeze (-5℃) or Freeze (-15~-23℃) to suit your needs.

## Slide 21
Item |  | Specification |  |  |  |  |  |  | 
Models |  | R*38T*3* | R*38T*0* R*38T*7* | R*38T*2* R*38T*6* | R*36T*0* R*36T*7* | R*36T*2* R*36T*6* | R*34T*3* | R*34T*0* R*34T*7* | R*33B*1*
Cooling system |  | Mono Cooling |  |  |  |  |  |  | 
Net Capacity | Total | 376 | 385 |  | 360 |  | 331 | 340 | 340
 | Freezer | 264 | 273 |  | 248 |  | 219 | 228 | 228
 | Refrigerator | 112 | 112 |  | 112 |  | 112 | 112 | 112
Net Dimension | Width (mm) | 595 |  |  | 595 |  | 595 |  | 595
 | Depth (mm) | 658 |  | 720 | 658 | 720 | 658 |  | 658
 | Height (mm) | 2030 |  |  | 1935 |  | 1853 |  | 1853
Handle Type |  | Recess | Recess | Bar | Recess | Bar | Recess | Recess | Side Recess
Water Dispenser |  | Yes | - | - | - | - | Yes | - | -
Weight | Set | 71 kg |  |  | 68 kg |  | 67 kg |  | 67
 | Packing | 74 kg |  |  | 71 kg |  | 70 kg |  | 70
Packing | Width (mm) | 637 |  |  | 637 |  | 637 |  | 637
 | Depth (mm) | 740 |  |  | 744 |  | 740 |  | 740
 | Height (mm) | 2108 |  |  | 2013 |  | 1935 |  | 1935
Rated Voltage and Frequency |  | AC 115 V / 60 Hz |  |  |  |  |  |  | 
 |  | AC 230 V / 50 Hz |  |  |  |  |  |  | 
Type Refrigerator |  | Indirect Cooling Method Refrigerator |  |  |  |  |  |  | 
2-2. Model Specification (R*38T*/R*36T*/R*34T*)
To do list
2. Product Specifications

## Slide 22
Item |  | Specification |  |  |  |  |  | 
Models |  | R*38A*9* | R*38A*B* | R*38A*C* | R*34A*9* | R*34A*B* | R*38A*9* | R*38A*B*
Cooling system |  | Mono Cooling |  |  |  |  | Twin Cooling | 
Net Capacity | Total | 385 |  | 385 | 340 |  | 382 | 
 | Freezer | 273 |  | 273 | 228 |  | 270 | 
 | Refrigerator | 112 |  | 112 | 112 |  | 112 | 
Net Dimension | Width (mm) | 595 |  | 595 | 595 |  | 595 | 
 | Depth (mm) | 658 |  | 658 | 658 |  | 658 | 
 | Height (mm) | 2030 |  | 2030 | 1853 |  | 2030 | 
Handle Type |  | Recess | Bespoke | Bespoke | Recess | Bespoke | Recess | Bespoke
Water Dispenser |  | Yes | - | - | Yes | - | Yes | -
Weight | Set | 71 kg |  |  | 67 kg |  | 71 kg | 
 | Packing | 74 kg |  |  | 70 kg |  | 74 kg | 
Packing | Width (mm) | 637 |  |  | 637 |  | 637 | 
 | Depth (mm) | 740 |  |  | 740 |  | 740 | 
 | Height (mm) | 2108 |  |  | 1935 |  | 2108 | 
Rated Voltage and Frequency |  | AC 115 V / 60 Hz |  |  |  |  |  | 
 |  | AC 230 V / 50 Hz |  |  |  |  |  | 
Type Refrigerator |  | Indirect Cooling Method Refrigerator |  |  |  |  |  | 
2-2. Model Specification (R*38A*/R*34A*)
To do list
2. Product Specifications

## Slide 23
To do list
2. Product Specifications
2-2. Model Specification (Twin Cooling)
Items |  |  | Specification |  |  | 
Model |  |  | R*38A****3 | R*38A****B | R*38A****A | R*38A****T
Cooling system |  |  | Twin Cooling |  |  | 
Energy Grade |  |  | C | B | A | A
 | Compressor | Model | NN54T9902AVAK3 |  | NN54T9602AVAK3 | NN54T9602AVAK3
 |  | Starting type | BLDC |  |  | 
 |  | Oil Charge | 200 ± 10cc |  |  | 
 | Evaporator | Freezer | Split Fin Type |  |  | 
 |  | Refrigerator | Split Fin Type |  |  | 
 | Condenser |  | Forced Convection Type |  |  | 
 | Dryer |  | Molecular sieve, XH-9, 6g |  |  | 
 | Capillary tube (D × L) |  | F : (0.75mm x 4000mm) R : (0.85mm x 4000mm) |  |  | 
 | Refrigerant |  | R-600a |  |  | 
 | Refrigerant Input Amount |  | 70g |  |  | 73g
Components for Freezer

## Slide 24
To do list
2. Product Specifications
Items |  |  | Specification |  |  |  | 
Model |  |  | R*38*****C | R*38*****2 | R*38*****D | R*38*****E | R*38*****F
Cooling system |  |  | Mono Cooling |  |  |  | 
Energy Grade |  |  | C | 2 | D | E | F
 | Compressor | Model | NN54T9902AVAK3 | NI34T9101ABTT1 |  | NI34T9101ADTT1 | NI34T9102ADTT1
 |  | Starting type | BLDC | BLDC |  | BLDC | BLDC
 |  | Oil Charge | 200 ± 10cc | 160 ± 10cc |  | 160 ± 10cc | 160 ± 10cc
 | Evaporator | Freezer | Split Fin Type |  |  |  | 
 |  | Refrigerator | - |  |  |  | 
 | Condenser |  | Forced Convection Type | Natural Convection Type |  |  | 
 | Dryer |  | Molecular sieve, XH-9, 6g |  |  |  | 
 | Capillary tube (D × L) |  | F : (0.75mm x 4000mm) | F : (0.75mm x 3500mm) |  |  | 
 | Refrigerant |  | R-600a |  |  |  | 
 | Refrigerant Input Amount |  | 70g | 54g |  |  | 
2-2. Model Specification (Mono Cooling)
Components for Freezer

## Slide 25
To do list
2. Product Specifications
Items |  |  | Specification |  |  | 
Model |  |  | R*36T****C | R*36T****D | R*36T****E | R*36T****F
Cooling system |  |  | Mono Cooling |  |  | 
Energy Grade |  |  | C | D | E | F
 | Compressor | Model | NN54T9902AVAK3 | NI34T9101ABTT1 | NI34T9101ADTT1 | NI34T9102ADTT1
 |  | Starting type | BLDC | BLDC | BLDC | BLDC
 |  | Oil Charge | 200 ± 10cc | 160 ± 10cc | 160 ± 10cc | 160 ± 10cc
 | Evaporator | Freezer | Split Fin Type |  |  | 
 |  | Refrigerator | - |  |  | 
 | Condenser |  | Forced Convection Type | Natural Convection Type |  | 
 | Dryer |  | Molecular sieve, XH-9, 6g |  |  | 
 | Capillary tube (D × L) |  | F : (0.75mm x 4000mm) | F : (0.75mm x 3500mm) |  | 
 | Refrigerant |  | R-600a |  |  | 
 | Refrigerant Input Amount |  | 70g | 54g |  | 
Components for Freezer
2-2. Model Specification (Mono Cooling)

## Slide 26
To do list
2. Product Specifications
Items |  |  | Specification |  |  | 
Model |  |  | R*34*****C | R*34*****D R*34*****1 | R*34*****E R*33*****E | R*34*****F R*33*****F
Cooling system |  |  | Mono Cooling |  |  | 
Energy Grade |  |  | C | D,1 | E | F
 | Compressor | Model | NN54T9902AVAK3 | NI34T9101ABTT1 | NI34T9102ADTT1 | 
 |  | Starting type | BLDC | BLDC | BLDC | 
 |  | Oil Charge | 200 ± 10cc | 160 ± 10cc | 160 ± 10cc | 
 | Evaporator | Freezer | Split Fin Type |  |  | 
 |  | Refrigerator | - |  |  | 
 | Condenser |  | Forced Convection Type | Natural Convection Type |  | 
 | Dryer |  | Molecular sieve, XH-9, 6g |  |  | 
 | Capillary tube (D × L) |  | F : (0.75mm x 4000mm) | F : (0.75mm x 3500mm) |  | 
 | Refrigerant |  | R-600a |  |  | 
 | Refrigerant Input Amount |  | 70g | 54g |  | 
Components for Freezer
2-2. Model Specification (Mono Cooling)

## Slide 27
2-2. Model Specification
To do list
2. Product Specifications
Items |  |  | Specification
 | Defrost Heater | FRE | 140W , AC 230V
 |  | REF | -
 | Preventing of FRE Defrost Heater | BIMETAL | Off: 60℃, On: 40℃ (AC 250V,3A / AC 125V,6A)
 |  | THERMO FUSE | 109 ~ 110℃ cut off
 | Rated Voltage |  | AC 230V / 50HZ
 | Motor | FRE | DC12V, BLDC(AIO Q7, Φ120), 2.5W
 |  | REF | -
 |  | CIRCUIT | DC12V, BLDC(C160N, Φ160), 1.32W
 |  | DAMPER | DC12V, Step Motor, H/T 1W
 | Lamp LED | FRE | -
 |  | REF | DC 12V, Max 199mA, 3PKGs
 | Door Switch | FRE | Reed switch (DC 200V, 0.5A, MDCG-4)
 |  | REF | Reed switch (DC 200V, 0.5A, MDCG-4)
 | Power Cord |  | AC 250V, 16A
 | Earth Screw |  | BSBN (BRASS SCREW)
Electric Components

## Slide 28
2. Product Specifications
2-3. Electric Parts Specification (Twin Cooling)
Items |  |  |  | Specification |  |  |  |  |  |  | 
Model |  |  |  | RB38*****3 |  | RB38*****B |  | RB38*****A |  | RB38*****T | 
 |  | Model | Temperature Selection | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃)
 |  | THERMISTOR (F-sensor) 502AT | -23℃ | -22.5 | -23.5 | -22.5 | -23.5 | -22.5 | -23.5 | -22.5 | -23.5
 |  |  | -19℃ | -18.5 | -19.5 | -18.5 | -19.5 | -18.5 | -19.5 | -18.5 | -19.5
 |  |  | -15℃ | -14.5 | -15.5 | -14.5 | -15.5 | -14.5 | -15.5 | -14.5 | -15.5
 |  | Model | Temperature Selection | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃)
 |  | THERMISTOR (R-sensor) 502AT | 1℃ | 0.0 | 2.0 | 0.0 | 2.0 | 0.0 | 2.0 | 0.0 | 2.0
 |  |  | 3℃ | 2.0 | 4.0 | 2.0 | 4.0 | 2.0 | 4.0 | 2.0 | 4.0
 |  |  | 7℃ | 6.0 | 8.0 | 6.0 | 8.0 | 6.0 | 8.0 | 6.0 | 8.0
 |  | First Defrost Cycle (Concurrent defrost of F and R) |  | 6hr ± 10 min |  |  |  |  |  |  | 
 |  | Defrost Cycle (FRE) |  | 6 ~ 100hr (vary according to the conditions used) |  |  |  |  |  |  | 
 |  | Defrost Cycle (REF) |  | 6 ~ 100hr (vary according to the conditions used) |  |  |  |  |  |  | 
 |  | Pause time |  | 5min ± 1 min |  |  |  |  |  |  | 
 | Defrost Sensor |  | Model | THERMISTOR (DKST1329GW) |  |  |  |  |  |  | 
 |  |  | SPEC | 13.29 ㏀±2% at 0℃ |  |  |  |  |  |  | 
 | Thermal-Fuse |  | Rated | 250V, 15A |  |  |  |  |  |  | 
 |  |  | Operating temperature | 109 or 110℃ |  |  |  |  |  |  | 
Room Temperature Sensor Components
Defrost Related Components
Freezer
Refrigerator
Defrost Cycle

## Slide 29
2. Product Specifications
2-3. Electric Parts Specification (Mono Cooling)
Items |  |  |  | Specification |  |  |  |  |  |  | 
Model |  |  |  | R*38*****C |  | R*34*****D |  | R*34*****E,F R*33*****E,F |  | RB36T****F | 
 |  | Model | Temperature Selection | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃)
 |  | THERMISTOR (F-sensor) 502AT | -23℃ | -22.0 | -24.0 | -22.0 | -24.0 | -22.0 | -24.0 | -22.0 | -24.0
 |  |  | -19℃ | -18.0 | -20.0 | -18.0 | -20.0 | -18.0 | -20.0 | -18.0 | -20.0
 |  |  | -15℃ | -14.0 | -16.0 | -14.0 | -16.0 | -14.0 | -16.0 | -14.0 | -16.0
 |  | Model | Temperature Selection | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃) | ON(℃) | OFF(℃)
 |  | THERMISTOR (R-sensor) 502AT | 1℃ | -1.0 | 3.0 | -1.0 | 3.0 | -1.0 | 3.0 | -1.0 | 3.0
 |  |  | 3℃ | 1.0 | 5.0 | 1.0 | 5.0 | 1.0 | 5.0 | 1.0 | 5.0
 |  |  | 7℃ | 5.0 | 9.0 | 5.0 | 9.0 | 5.0 | 9.0 | 5.0 | 9.0
 |  | First Defrost Cycle (Concurrent defrost of F and R) |  | 6hr ± 10 min |  |  |  |  |  |  | 
 |  | Defrost Cycle (FRE) |  | 6 ~ 99hr (vary according to the conditions used) |  |  |  |  |  |  | 
 |  | Defrost Cycle (REF) |  | - |  |  |  |  |  |  | 
 |  | Pause time |  | 5min ± 1 min |  |  |  |  |  |  | 
 | Defrost Sensor |  | Model | THERMISTOR (DKST1329GW) |  |  |  |  |  |  | 
 |  |  | SPEC | 13.29 ㏀±2% at 0℃ |  |  |  |  |  |  | 
 | Thermal-Fuse |  | Rated | 250V, 15A |  |  |  |  |  |  | 
 |  |  | Operating temperature | 109 or 110℃ |  |  |  |  |  |  | 
Room Temperature Sensor Components
Defrost Related Components
Freezer
Refrigerator
Defrost Cycle

## Slide 30
2-4. Dimensions of Refrigerator
2. Product Specifications

## Slide 31
2-4. Dimensions of Refrigerator
2. Product Specifications

## Slide 32
2-5. Refrigerant Route in Refrigeration cycle (Twin Cooling)
2. Product Specifications
To do list
32
Compressor
Condenser
Hot Pipe
Fre Capillary Tube
Fre Evaporator
Suction Pipe
Connect Suction Pipe
Compressor
Cluster Pipe
Dryer
Step Valve
Ref Capillary Tube
Ref Evaporator
[Energy C grade]
[Energy B, A grade]
Compressor
Condenser
Hot Pipe
Fre Capillary Tube
Fre Evaporator
Suction Pipe
Connect Suction Pipe
Compressor
Dryer
Step Valve
Ref Capillary Tube
Ref Evaporator
[Energy T grade]
Compressor
Condenser
Hot Pipe
Fre Capillary Tube
Fre Evaporator
Suction Pipe
Connect Suction Pipe
Compressor
Dryer
Step Valve
Ref Capillary Tube
Ref Evaporator
Cluster Pipe

## Slide 33
2-5. Refrigerant Route in Refrigeration cycle (Mono Cooling)
2. Product Specifications
To do list
33
Compressor
Condenser
Hot Pipe
Fre Capillary Tube
Freezer Evaporator
Suction Pipe
Connect Suction Pipe
Compressor
Cluster Pipe
Dryer
Step Valve
Compressor
Immersion pipe
Hot Pipe
Fre Capillary Tube
Freezer Evaporator
Suction Pipe
Connect Suction Pipe
Compressor
Cluster Pipe
Dryer
[Energy C grade]
[Energy D,E,F,1,2 grade]

## Slide 34
2. Product Specifications
To do list
34
Condenser
Compressor
Hot Pipe
Fre Evap
Cluster Pipe
Dryer
Step Valve
Capillary Tube
2-6. Principle Of Freezer (Twin Cooling C grade)

## Slide 35
2. Product Specifications
To do list
35
2-6. Principle Of Freezer (Twin Cooling B,A grade)
Condenser
Compressor
Hot Pipe
Fre Evap
Dryer
Step Valve
Capillary Tube

## Slide 36
2. Product Specifications
To do list
36
2-6. Principle Of Freezer (Twin Cooling T grade)
Condenser
Compressor
Hot Pipe
Fre Evap
Dryer
Step Valve
Capillary Tube
Cluster Pipe

## Slide 37
2-6. Principle Of Freezer (Mono Cooling)
2. Product Specifications
To do list
37
Condenser
Compressor
Hot Pipe
Fre Evap
Cluster Pipe
Dryer
Step Valve
Capillary Tube

## Slide 38
2. Product Specifications
2-7. Operation theory of refrigeration cycle components
To do list
38
■ Condenser
1) Role: A device which radiates heat to the outside (water/air) to make liquid state for the high temperature / high pressure gas refrigerant discharged from compressor
2) Types
A. Air-cooling Type : Condense air by circulating naturally or manually.
1) Natural Convection Type : Used for the household refrigerator which has small condensing capacity.
2) Manual Convection Type : Circulate air manually by FAN-Motor (Large capacity)
B. Water-cooling Type : Make cooling water pass through the pipe in the condenser (Large capacity)
※ Location
① CLUSTER heat-radiating type : All Pipes effective for radiating heat are formed in the right/left, and front side of refrigerator with hard urethanes and radiate heat through the whole surfaces of cabinet to ambient air.
② Install the condenser on the outside of the product. (An old model)
③ Make them cluster at the lower part of product and radiate heat manually by fan.
※ Radiate condensed potential heat up to liquefy completely and make change the state without changing the gas temperature itself.
※ Pipe thickness
① Micro-channel tube: 0.34mm ② Steel Pipe : 0.5, 0.7mm ③ Capillary : About 0.4~0.8mm
※ Condenser length
① CONDENSER : 0.32m × 14Pcs (Parallel) ② HOT-PIPE : 6.28m

## Slide 39
2. Product Specifications
2-7. Operation theory of refrigeration cycle components
To do list
39
■ Capillary
1) Role: A device which makes low temperature and pressure refrigerant by reducing the pressure the normal temperature / high pressure liquid refrigerant condensed from condenser, and supply it to the evaporator.
A. To evaporate more lower temperature in case of evaporation.
B. It flows to the evaporator without back flowing to condenser, if compressor stops, and the difference of pressure between high pressure and low pressure is small so it is easy to operate the compressor again.
2) Outline
A. Thickness : About 0.4~0.8mm
B. Length : It is changeable to low temperature and pressure (10->5ßΠ/ß≤) depends on the 2M
of thin and long copper pipe wall resistance.

## Slide 40
2. Product Specifications
2-7. Operation theory of refrigeration cycle components
To do list
40
■ Evaporator
1) Role: As the low pressure liquid refrigerant flowed from capillary absorbs heat inside of the refrigerator, it becomes low pressure gas and refrigerate the foods.
2) Theory: The low pressure refrigerant flowed to evaporator operates cooling which takes ambient evaporated potential heat with maintaining the evaporation up to evaporate completely.
3) Types:
A. ROLL-BOND Evaporator → Direct Cooling
☞ Rolled and adhere the 2 aluminum plate and then make refrigerant passage.
B. FIN-PIPE Evaporator → Indirect cooling
☞ A small aluminum plate on the aluminum pipe to increase the cooling effect.
■ Compressor
1) Role: It operates same as pump which pull out the subterranean water. It inhales the low temperature and pressure refrigerant gas (flowed out) from evaporator and make high temperature and pressure refrigerant liquid in the compressor and send it to the condenser.
2) Type
A. Back-and-forth motion type: A method that pistol makes back-and-forth motion through shaft and cylinder of motor rotation and compresses. ※ Used for household refrigerant
B. Rotary Type: A method that inhales the refrigerant gas through the gap between the outside of rotor electric attached on the shaft (rotation axis) and the inside of cylinder and compresses.
C. Centrifugal Type

## Slide 41
2. Product Specifications
2-7. Operation theory of refrigeration cycle components
To do list
41
■ Dryer
1) Role: Absorb the moisture from the refrigerant that refrigeration cycle circulates and eliminate the foreign substance.
2) Structure: If even some moisture is included refrigerant is impossible to circulate by freezing the small capillary outlet, so silica gel or molecular sieve is (included and) sealed to absorb the internal moisture, and install a minute net to eliminate the foreign substance.

## Slide 42
2-8. Interior Views
To do list
2. Product Specifications

## Slide 43
Press the ‘ O ’ key to blink the Fridge temperature indicator(1).
When the Fridge temperature indicator blinks, press the 'O' key once to
blink the Freezer temperature indicator(2). In other words, whenever you
press the 'O' key, the Fridge temperature display unit and the Freezer temperature display unit alternate and flashes.
3. Functions & Features
3-1. Control Display
1
‘O’ button
Note
Each time you press a button on the control panel, you will hear a short beep.
When you do not press any button, all LEDs become turned off for the minimum energy consumption.
When the Fridge temperature indicator blinks, press the '<' key to set it as follows.
Vacation → 7℃ → 6℃ → 5℃ → 4℃ → 3℃ → 2℃ → 1℃ → PowerFridge
When the Fridge temperature indicator blinks, press the ‘>' key to set it as follows.
PowerFridge → 1℃ → 2℃ → 3℃ → 4℃ → 5℃ → 6℃ → 7℃ → Vacation
When the Freezer temperature indicator blinks, press the '<' key to set it as follows.
(1) -15℃ → -16℃ → -17℃ → -18℃ → -19℃ → -20℃ → -21℃ → -22℃ → -23℃ → PowerFreezer
(2) Fridge → Chill → Soft Freeze → -15℃ → -16℃ → -17℃ → -18℃ → -19℃ → -20℃ → -21℃ → -22℃ → -23℃ → PowerFreezer
When the Freezer temperature indicator blinks, press the ‘>' key to set it as follows.
(1) PowerFreezer → -23℃ → -22℃ → -21℃ → -20℃ → -19℃ → -18℃ → -17℃ → -16℃ → -15℃
(2) PowerFreezer → -23℃ → -22℃ → -21℃ → -20℃ → -19℃ → -18℃ → -17℃ → -16℃ → -15℃ → Soft Freeze → Chill → Fridge
After completing the desired temperature setting, press ‘O’ or waiting the blinking stops and the temperature setting ends.
‘<’ ‘>’ button

## Slide 44
While Vacation function is activated, refrigerator will set the temperature to 15 °C to minimize the power consumption when you are going on a long vacation or business trip or you do not need to use the refrigerator.
While Vacation function is activated, freezer compartment remains on. Vacation function will be automatically deactivated if you adjust fridge temperature while Vacation function is on. Make sure to remove foods in the fridge compartment before using Vacation function.
3. Functions & Features
3-1. Control Display
1
Vacation
PowerFridge speeds up the cooling process at maximum fan speed. The fridge keeps running at full speed for two and a half hours and
then returns to the previous temperature
2
PowerFridge
Power Freeze speeds up the freezing process at maximum fan
speed. The freezer keeps running at full speed for 50 hours and
then returns to the previous temperature.
3
PowerFreezer
Normally, this icon is off. But If the door is left open for more than 2 minutes, the alarm will sound with this Door Alarm icon blinking.
If the door is left open for 5 minutes, internal light will blink for 5 minutes and turn off.
4
Door Alarm

## Slide 45
3. Functions & Features
3-2. Knob Control
If you are going on vacation or a business trip, or if you do not intend to use the fridge for an extended time, use the Vacation mode.
To activate the Vacation mode, turn the Fridge/Freezer Control dial to . The fridge temperature will be controlled under 15 °C and the freezer temperature will be controlled under -19 °C.
1
Vacation

## Slide 46
4. Disassembly and Assembly
4-1. Precaution

## Slide 47
4. Disassembly and Assembly
4-1. Precaution

## Slide 48
IMAGE | ITEM | USE
 | Phillips Head Driver | Use for assembling and disassembling of screw
 | Flat Head Driver | Use for assembling and disassembling of HomeBar, Dispenser, Deli Cartessen Box, Main PBA etc...
 | Socket Wrench Ø10mm | Use for assembling and disassembling of Door Hinge
- Required Tools
4. Disassembly and Assembly
4-1. Precaution
To do list
48

## Slide 49
4. Disassembly and Assembly
4-2. Assy PCB
To do list
49
Part name | How to do | Descriptive Picture
Assy PCB | [Disassembly] 1. Loosen screw 3ea on Cover PCB with the (+) screwdriver and Open | 
 | 2. Unsnap connectors of PCB. | 
 | 3. Push 1 hooks to upside and pull out PCB outside. | 
Be sure to unplug the power cord before performing the operation above.

## Slide 50
4. Disassembly and Assembly
4-2. Assy PCB
To do list
50
Part name | How to do | Descriptive Picture
Assy PCB | [Assembly] 1. Insert PCB low-side in the 2ea fixer | 
 | 2. Push 1 hooks to upside and push PCB in the hooks. | 
 | 3. Snap the connectors of PCB | 
 | 4. Assemble Cover PCB and fasten screw 3ea with the (+) screwdriver. | 
Be sure to unplug the power cord before performing the operation above.

## Slide 51
Part name | How to do | Descriptive Picture
Assy Top Table | 1. Open the door and press the Cover Wire to remove it from the Cap Door. (If there is no cover hinge, Don’t disassemble Cover Wire) | 
 | 2. Remove screws using (+) screwdriver. (2ea) | 
 | 3. Disassemble Assy Top Table from Cabinet after push Cover Hinge. (If there is no cover hinge, just disassemble Top Table) | 
 | 4. Disconnect the wire connectors from the door and the atop cover. (If there is no cover hinge, go next step) | 
4. Disassembly and Assembly
4-3. Assy Top Table
To do list
51
Be sure to unplug the power cord before performing the operation above.

## Slide 52
4. Disassembly and Assembly
4-3. Assy Top Table
To do list
52
Part name | How to do | Descriptive Picture
Assy Top Table | 5. Disconnect the wire connectors from the Reed Switch. | 
 | 6. Disconnect the Temp Sensor from the Assy Top Table. (push the temp sensor to hook) | 
 | 7. Disconnect the wire connectors from the WIFI MODULE. (If there is no WIFI MODULE, go next step) | 
 | 8. Disconnect the wire connectors from the BUZZER. | 
 | 9. Check complete released state from Cabinet. | 
 | 10. If you want Assemble, do reverse this process. | 
PUSH

## Slide 53
Part name | How to do | Descriptive Picture
Reed Switch | Disconnect the wire connectors from the Reed Switch. | 
 | 2. Push the hook to remove the Reed Switch from the Assy Top Table. | 
 | 3. Check complete released state from Assy Top Table. | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-4. Reed Switch
To do list
53
Be sure to unplug the power cord before performing the operation above.

## Slide 54
Part name | How to do | Descriptive Picture
Temp Sensor | Push the Temp Sensor at hook on top table. | 
 | 2. Loosen screw 5ea on Cover PCB with the (+) screwdriver and Open. | 
 | 3. Disconnect the Cover Wire from the Case PCB. | 
 | 4. Disconnect the Temp Sensor wire connectors from the Assy Wire Harness. | 
 | 5. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-5. Temp Sensor
To do list
54
PUSH
Be sure to unplug the power cord before performing the operation above.

## Slide 55
4. Disassembly and Assembly
4-6. Buzzer
To do list
55
Part name | How to do | Descriptive Picture
BUZZER | Disconnect the wire connectors from the BUZZER. | 
 | 2. Push the hook to remove the BUZZER from the Assy Top Table. | 
 | 3. Check complete released state from Assy Top Table. | 
 | 4. If you want Assemble, do reverse this process. | 
Be sure to unplug the power cord before performing the operation above.

## Slide 56
4. Disassembly and Assembly
4-7. Wi-fi Module
To do list
56
Part name | How to do | Descriptive Picture
Wi-fi Module | Disconnect the wire connectors from the Wifi MODULE. | 
 | 2. Push the hook to remove the WIFI MODULE from the Assy Top Table. | 
 | 3. Check complete released state from Assy Top Table. | 
 | 4. If you want Assemble, do reverse this process. | 
Be sure to unplug the power cord before performing the operation above.

## Slide 57
Part name | How to do | Descriptive Picture
Hinge Upp | 1. Disassemble Assy Top Table (Refer to the previous explanation “Disassembly and Reassembly way for 4-3. Assy top table”) | 
 | 2. Remove 2 bolts and Hinge Upp from cabinet. | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-8. Hinge Upp
To do list
57
Before Hinge Remove, Must fix door on the set using Tape for safety.
(above Width 40㎜ and Must be attached at least 3 times at the minimum upper / middle / lower position.)
Must working more than 2 people.
One person grab the door to prevent falling door.

## Slide 58
Part name | How to do | Descriptive Picture
Refrigerator Door | 1. Disassemble Assy Top Table. (Refer to the previous explanation “Disassembly and Reassembly way for 4-3. Assy top table”) | 
 | 2. Disassemble Hinge Upp. (Refer to the previous explanation “Disassembly and Reassembly way for 4-6. Hinge Upp”) | 
 | 3. Open the fridge door, and then lift the door to remove it from the Hinge Mid. (※ Keep the door in a safe place) | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-9. Refrigerator Door
To do list
58
Must working more than 2 people.
One person grab the door to prevent falling door.

## Slide 59
Part name | How to do | Descriptive Picture
Hinge Mid | 1. Disassemble Refrigerator Door. (Refer to the previous explanation “Disassembly and Reassembly way for 4-7. Refrigerator Door”) | 
 | 2. Remove 1 screw and 2 bolts. | 
 | 3. Remove Hinge Mid from cabinet. | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-10. Hinge Mid
To do list
59
Before Hinge Remove, Must fix door on the set using Tape for safety.
(above Width 40㎜ and Must be attached at least 3 times at the minimum upper / middle / lower position.)
Must working more than 2 people.
One person grab the door to prevent falling door.

## Slide 60
4. Disassembly and Assembly
4-11. Reed Switch (Non Bespoke)
Part name | How to do | Descriptive Picture
Reed Switch | [Replacing Reed Switch] 1. Insert a flat-head screwdriver on the slot as shown and lift it to disassemble cap of Reed Switch. | 
 | 2. Disconnect the wire connectors from the Reed Switch and the Refrigerator door. | 
 | 3. Connect the wire connectors from the Changed Reed Switch and the door. | 
 | 4. Insert the rib of the cap of Reed Switch to the pocket of Cap door and press opposite side of the rib until fully fixed. | 
60
To do list

## Slide 61
4. Disassembly and Assembly
4-11. Reed Switch (Bespoke)
Part name | How to do | Descriptive Picture
Reed Switch | [Replacing Reed Switch] 1. Insert a flat-head screwdriver on the slot as shown and lift it to disassemble cap of Reed Switch. | 
 | 2. Disconnect the wire connectors from the Reed Switch and the Cabinet. | 
 | 3. Connect the wire connectors from the Changed Reed Switch and the Cabinet. | 
 | 4. Insert the rib of the cap of Reed Switch to the pocket of Cabinet and press opposite side of the rib until fully fixed. | 
61
To do list

## Slide 62
4. Disassembly and Assembly
4-12. Freezer Door
Part name | How to do | Descriptive Picture
Freezer Door | [Disassemble Hinge Low] 1. Open the freezer door, and then use a screwdriver to remove the screws fastening the Hinge Low. | 
 | 2. With the freezer door sitting on the bottom hinge, slowly pull the bottom hinge to remove it from the holder on the bottom of the refrigerator. Once the bottom hinge is removed from the holder, remove it from the freezer door, and then pull the freezer door down to remove it from the middle hinge. | 
 | 3. If you want Assemble, do reverse this process. | 
62
To do list
To prevent the freezer door from falling, make sure to hold the freezer door tight until it is safely removed from the middle hinge.
Must working more than 2 people.
One person grab the door to prevent falling door.

## Slide 63
4. Disassembly and Assembly
63
To do list
4-13. Bespoke Panel Door(Ref)
Part name | How to do | Descriptive Picture
Bespoke Panel Door(Ref) | 1. Disassemble 3 pieces cover cap door. - Use “-” driver | 
 | 2. Disassemble the custom panel . - Attach and closed lever of Suction Cup on upper corner. - Pull the custom panel infront. | 
 | 3. Carefully put the custom panel down (※ Keep the door in a safe place) | 
 | 4. If you want Assemble, Start from bottom. Insert low trim on the ref door. And then do reverse this process. (※ Images on left is just for explanation) | 

## Slide 64
4. Disassembly and Assembly
4-14. Bespoke Panel Door(Fre)
64
To do list
Part name | How to do | Descriptive Picture
Bespoke Panel Door(Fre) | 1. Disassemble 3 pieces cap screw. - Use “-” driver | 
 | 2. Disassemble the custom panel . - Attach and closed lever of Suction Cup on lower corner. - Pull the custom panel infront. | 
 | 3. Carefully put the custom panel down (※ Keep the door in a safe place) | 
 | 4. If you want Assemble, Start from top of the door. Insert up trim on the ref door. And then do reverse this process. | 

## Slide 65
4. Disassembly and Assembly
4-15. Door Gasket
Part name | How to do | Descriptive Picture
Door Gasket | [Disassembly] 1. Pull the corners of gasket. | 
 | 2. Pull the corners of gasket. | 
 | [Assembly] 1. Press the corners of gasket. | 
 | 2. Press the rest of gasket. | 
65
To do list

## Slide 66
Part name | How to do | Descriptive Picture
Door Handle (Bar) | Insert a flat-head screwdriver on the slot as shown and unlock the caps | 
 | 2. Remove screws by turning to counterclockwise, and take off the Assy Handle by pulling out. | 
 | 3. If you want Assemble, do reverse this process | 
4. Disassembly and Assembly
4-16. Door Handle (Bar)
To do list
66

## Slide 67
Part name | How to do | Descriptive Picture
Assy Case Veg Up | 1. Take out the Assy Case Veg Up to the front. | 
 | 2. Lift up the front part and pull out the Assy Case Veg Up | 
 | 3. Lift up the front part of Case Divider | 
 | 4. Lift up the back of the Case Divider and disassemble. | 
 | 5. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-17. Assy Case Veg Up
To do list
67

## Slide 68
Part name | How to do | Descriptive Picture
Case Veg Low | 1. Take out the Case Veg Low to the front. | 
 | 2. Lift up the front of Case Veg Low. | 
 | 3. Pull out the Case Veg Low. | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-18. Case Veg Low
To do list
68

## Slide 69
Part name | How to do | Descriptive Picture
Tray Freezer | 1. Take out the Tray Freezer to the front. | 
 | 2. Lift up the front of Tray Freezer. | 
 | 3. Pull out the Tray Freezer. | 
 | 4. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-19. Tray Freezer
To do list
69

## Slide 70
Part name | How to do | Descriptive Picture
Shelf Ref | 1. Lift the back of the Shelf. | 
 | 2. Pull the Shelf. | 
 | 3. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-20. Shelf Ref
To do list
70

## Slide 71
Part name | How to do | Descriptive Picture
Wine Rack | 1. Lift the back of the Wine Rack. | 
 | 2. Pull the Wine Rack. | 
 | 3. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-21. Wine Rack
To do list
71

## Slide 72
Part name | How to do | Descriptive Picture
Shelf Veg Up | 1. Lift the front of the Shelf Veg Up. | 
 | 2. Pull the Shelf Veg Up. | 
 | 3. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-22. Shelf Veg Up
To do list
72

## Slide 73
Part name | How to do | Descriptive Picture
Shelf Veg Low | 1. Pull the Case Veg Up | 
 | 2. Lifts up the Case Veg Up and removes it. | 
 | 3. Lift the front of the Shelf Veg Low. | 
 | 4. Pull the Shelf Veg Low. | 
 | 5. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
4-23. Shelf Veg Low
To do list
73

## Slide 74
4. Disassembly and Assembly
4-24. Cover Evap Ref (Twin Cooling)
To do list
74
Part name | How to do | Descriptive Picture
Cover Evap Ref | 1. Remove Screws using (+) screwdriver. (2ea) | 
 | 2. Remove the Cover Evap Ref. (Push the side hook and pull the Cover conv) | 
 | 3. Disassemble the Sensor Temp/Damper housing. | 
 | 4. Pull the bottom of Cover Evap Ref and Disassemble it. | 
 | 5. If you want Assemble, do reverse this process. | 
Before doing the above, make sure that the unit is unplugged.

## Slide 75
4. Disassembly and Assembly
4-25. Sensor temp-Ref (Twin Cooling)
To do list
75
Part name | How to do | Descriptive Picture
Sensor temp Ref | [Replacing Sensor temp] 1. Sensor temp located on right side insulation cover evap ref. | 
 | 2. Unwind the Sensor Temp Wire. | 
 | 3. Disassemble the Insulation cover evap ref from Cover evap ref. (Caution to disassemble side hook(picture) not to damage Ins cover evap ref.) | 
 | 4. Unwind the Sensor Temp Wire. | 
 | 5. Disassemble Sensor Temp and replace it with new one. (Also, disassemble the wire of Sensor Temp) | 
 | 6. If you want Assemble, do reverse this process. | 

## Slide 76
4. Disassembly and Assembly
4-26. Motor Fan-Ref (Twin Cooling)
To do list
76
Part name | How to do | Descriptive Picture
Motor Fan Ref | [Replacing Fan] 1. Disassemble Assy case motor from Liner. (remove screw 2ea) | 
 | 2. Remove Bolts using (+) screwdriver. (2ea) | 
 | 3. Disassemble the plate drain from the bracket motor . | 
 | 4. Unwind the Fan Wire. Remove Bolts using (+) screwdriver. (2ea) | 
 | 5. Remove Bolts using (+) screwdriver. (3ea) Disassemble the Fan from Bracket motor and replace it with new one. | 
 | 6. If you want Assemble, do reverse this process. (go through 1~5 in backwards, No.3 seal reuse.) | 

## Slide 77
4. Disassembly and Assembly
4-27. Cover Multi Ref (Mono Cooling)
To do list
77
Part name | How to do | Descriptive Picture
Cover Multi Ref | 1. Remove Screws using (+) screwdriver. (2ea) | 
 | 2. Remove the Cover conv multi. (Push the side hook and pull the Cover conv) | 
 | 3. Disassemble the Sensor Temp/Damper housing. | 
 | 4. Pull the bottom of Cover Multi-ref and Disassemble it. | 
 | 5. If you want Assemble, do reverse this process. | 
Before doing the above, make sure that the unit is unplugged.

## Slide 78
4. Disassembly and Assembly
4-27. Cover Multi Ref (RB33A*)
To do list
78
Part name | How to do | Descriptive Picture
Cover Multi Ref | 1. Remove Screws using (+) screwdriver. (2ea) | 
 | 2. Pull the bottom of Cover Multi-ref and Disassemble it. | 
 | 3. Turn left Cover multi-ref and Disassemble sensor, damper and Knob housing. | 
 | 4. If you want Assemble, do reverse this process. | 
Before doing the above, make sure that the unit is unplugged.

## Slide 79
4. Disassembly and Assembly
To do list
79
Part name | How to do | Descriptive Picture
Sensor temp Ref | [Replacing Sensor temp] 1. Remove Bolts using (+) screwdriver. (4ea) | 
 | 2. Disassemble the Cover multi ref B. | 
 | 3. Disassemble the Insulation multi ref A/B & Cover multi A. (Caution to disassemble side hook(picture) not to damage Ins multi ref A.) | 
 | 4. Unwind the Sensor Temp Wire. | 
 | 5. Disassemble Sensor Temp and replace it with new one. (Also, disassemble the wire of Sensor Temp) | 
 | 6. If you want Assemble, do reverse this process. | 
[Sensor wire_1]
[Sensor wire_2]
4-28. Sensor temp Ref (Mono Cooling)

## Slide 80
4. Disassembly and Assembly
4-29. Damper (Mono Cooling)
To do list
80
Part name | How to do | Descriptive Picture
Damper | [Replacing Damper] 1. Remove Bolts using (+) screwdriver. (4ea) | 
 | 2. Disassemble the Cover multi ref B. | 
 | 3. Disassemble the Insulation multi ref B and A. (Do not cut the seal. Detach slightly not to damage.) | 
 | 4. Unwind the Motor Damper Wire. | 
 | 5. Disassemble the Motor Damper from Insulation damper and replace it with new one. | 
 | 6. If you want Assemble, do reverse this process. (go through 1~5 in backwards, No.3 seal reuse.) | 
A
B
[damper wire]
Insulation Damper

## Slide 81
4. Disassembly and Assembly
4-30. Knob (RB33A*)
To do list
81
Part name | How to do | Descriptive Picture
Knob | [Replacing Knob] 1. Remove Knob Dial from the COVER DAMPER. Pull the Knob Dial. | 
 | 2. Unwind the Knob PCB wire. | 
 | 3. Remove Knob PCB from the COVER DAMPER. and replace it with new one. | 
 | 4. If you want Assemble, do reverse this process. | 
[Knob PCB wire]
[Knob PCB ]

## Slide 82
4. Disassembly and Assembly
4-31. Cover Evap Freezer
To do list
82
Part name | How to do | Descriptive Picture
Cover Evap Fre | [Cover Evap fre Disassembly] 1. Remove Bolts using (+) screwdriver. (3ea) | 
 | 2. Pull the bottom of Cover Evap-fre and Disassemble it. | 
 | 3. Disassemble the Sensor Temp/Fan housing. | 
 | 4. If you want Assemble, do reverse this process. | 
Before doing the above, make sure that the unit is unplugged.

## Slide 83
4. Disassembly and Assembly
4-32. Motor Fan
To do list
83
Part name | How to do | Descriptive Picture
Motor Fan | [Replacing Motor fan] 1. Remove Plate Evap rear.(slide) | 
 | 2. Detach slightly the seal around the cover evap. | 
 | 3. Remove Bolts using (+) screwdriver. (3ea) | 
 | 4. Disassemble cover evap rear and wire arrangement. | 
 | 5. Remove Bolts using (+) screwdriver(3ea) and fan. | 
 | 6. If you want Assemble, do reverse this process. (go through 1~5 in backwards, No.2 seal reuse) | 

## Slide 84
4. Disassembly and Assembly
4-33. Sensor temp Fre
To do list
84
Part name | How to do | Descriptive Picture
Sensor temp Fre | [Replacing Sensor Temp] 1. Remove Plate Evap rear. (disassemble the hooks) | 
 | 2. Detach slightly the seal around the cover evap. | 
 | 3. Remove Bolts using (+) screwdriver. (3ea) | 
 | 4. Disassemble cover evap rear. | 
 | 5. Remove Sensor Temp and replace it with new one. | 
 | 6. If you want Assemble, do reverse this process. (go through 1~5 in backwards, No.2 seal reuse) | 

## Slide 85
Part name | How to do | Descriptive Picture
Evap Ref (Sensor Temp) | 1. Remove the housing connector part right one. | 
 | 2. Remove the evaporator out from four Fixer. | 
 | [Replacing Sensor Temp] 1. Cutting cable tie and remove the housing connector | 
 | 2. Separate fixer and change Sensor Temp | 
4. Disassembly and Assembly
4-34. Evap Ref (Sensor Temp)
To do list
85

## Slide 86
Part name | How to do | Descriptive Picture
Evap Fre (Sensor Temp) | 1. Remove the housing connector part left one. | 
 | 2. Remove the evaporator by pulling the lower part of the evaporator while lifting it up. | 
 | [Replacing Sensor Temp] 1. Cutting cable tie and remove the housing connector | 
 | 2. Separate fixer and change Sensor Temp | 
4. Disassembly and Assembly
4-35. Evap Fre (Sensor Temp)
To do list
86

## Slide 87
Part name | How to do | Descriptive Picture
LED Lamp | [Disassembly of LED Lamp] 1. Insert the small flat-head screwdriver at inert point’s gap between liner and cover lamp | 
 | 2. Pull back the cover lamp with screwdriver | 
 | 3. Repeat twice more the #2, #3 work | 
 | 4. Separate the Cover lamp from Liner | 
4. Disassembly and Assembly
To do list
4-36. LED Lamp
87
Insert point
insert
Pull back
Repeat
Separate

## Slide 88
Part name | How to do | Descriptive Picture
LED Lamp | 5. Pull up the connector area to delete the connector from led lamp | 
 | 6. Push the hook trigger and pull the connector to separate | 
 | 7. Slightly lift the socket side | 
 | 8. Slide out the led lamp from cover lamp | 
4. Disassembly and Assembly
To do list
4-36. LED Lamp
88
Push and pull

## Slide 89
Part name | How to do | Descriptive Picture
LED Lamp | [Assembly of LED Lamp] 1. Slide in the led lamp to cover lamp (Led must located under the hook feature of cover lamp) | 
 | 2. Before connecting the connector, slightly bend up the led socket side and connect to connector | 
 | 3. Locate the cover lamp at liner and hook the back side hook first | 
 | 4. Hook the front 3 point. | 
4. Disassembly and Assembly
To do list
4-36. LED Lamp
89
Check point

## Slide 90
Part name | How to do | Descriptive Picture
Water Dispenser | [Disassembly of Water Dispenser] 1. Remove Bolts using (+) screwdriver. (2ea) | 
 | 2. Put your hand inside the cover and pull it forward. | 
 | 3. Disassemble the assy cover dispenser | 
 | [Assembly of Water Dispenser] 1. Locate the assy cover dispenser at the dispenser | 
 | 2. Press your hand on the back to get hooks. 3. . Assemble screw bolts. (2ea) | 
4. Disassembly and Assembly
To do list
4-37. Water Dispenser
90

## Slide 91
Part name | How to do | Descriptive Picture
Water Tank | 1. Hold both sides of the water tank with hands and pull it forward. | 
 | 2. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
To do list
4-38. Water Tank
91

## Slide 92
Part name | How to do | Descriptive Picture
Cover Control | 1. Remove lower side Inlay. | 
 | 2. Push between Reflector and Case with the (-) screwdriver. | 
 | 3. Hit on the end of the screwdriver. | 
 | 4. Pull Cover Control out and Disconnect Housing. | 
 | 5. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
To do list
4-39. Cover Control (Door)
92
inlay

## Slide 93
Part name | How to do | Descriptive Picture
Cover Control | 1. Remove lower side Inlay. | 
 | 2. Push between Reflector and Case with the (-) screwdriver. | 
 | 3. Pull display out . | 
 | 4. Disconnect Housing. | 
 | 5. If you want Assemble, do reverse this process. | 
4. Disassembly and Assembly
To do list
4-40. Cover Control (Liner)
93
inlay

## Slide 94
4. Disassembly and Assembly
4-41. Motor Fan (Machine Compartment)
To do list
94
Part name | How to do | Descriptive Picture
Motor Fan | 1. Unscrew 5 Point of Cover comp | 
 | 2. Remove 1 screw. | 
 | 3. Remove the HOUSING CONNECTOR. (Refer to the picture) | 
 | 4. Pull forward to separate the Fan | 
Be careful not to damage from the inner hole of cover comp.

## Slide 95
4. Disassembly and Assembly
To do list
95
Part name | How to do | Descriptive Picture
Compressor | 1. Cut off the LOKRING connecting the COMP and the CONDENSER with a Pipe Cutter. (Red-line marking points) | 
 | 2. Cut off the connecting the COMP and the SUCTION CONNECT with a Pipe Cutter. (Red-line marking points) | 
 | 3. Link the COMP and the CONDENSER with a PIPE-CONNECTOR (DA81-05659A) by brazing the joint areas. | 
4-42. Compressor
This appliance contains a small amount of isobutane refrigerant (R-600a), a natural gas with high environmental compatibility that is, however, also flammable. When transporting and installing the appliance, care should be taken to ensure that no parts of the refrigerating circuit are damaged.

## Slide 96
4. Disassembly and Assembly
4-43. Relay O/L
To do list
96
Part name | How to do | Descriptive Picture
Relay O/L | 1. Remove Cover Relay. | 
 | 2. Disassemble Housing Connector from Comp | 
Before doing the above, make sure that the
unit is Unplugged.

## Slide 97
4. Disassembly and Assembly
To do list
97
WARNING
▪ Tilting/laying the refrigerator requires a minimum of 2 people.
▪ Disconnect power source before reversing doors.
Read these instructions completely and carefully
4-44. Reversing the Door swing
CAUTION
▪ Throughout the entire reversing procedure, keep all the small parts (screws, caps, etc.) of the refrigerator away
from children or infants for safety reasons.
▪ Make sure to keep all the screws and other removed parts in a safe place during the door reversal process.

## Slide 98
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 1. With the fridge door closed, use a Phillips screwdriver to remove the screws fastening the top cover. | 
 | 2. Gently lift the top cover and place it on top of the refrigerator. - Be careful when you lift the top cover. There is a wire connected underneath it. | 
 | 3. Disconnect the wire connectors from the door and the top cover. - This step may not apply to some models. | 
98
4-44. Reversing the Door swing

## Slide 99
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 4. Use a socket wrench (8 mm) to remove the screws fastening the top hinge. * CAUTION To prevent the fridge door from falling, make sure to hold it tight while removing the screws. | 
 | 5. Open the fridge door, and then lift the door to remove it from the middle hinge. Keep the door in a safe place. * CAUTION The door is heavy. To prevent damage or injury, use caution while removing the door. | 
 | 6. Open the freezer door, and then use a socket wrench (8 mm) to remove the screws fastening the bottom hinge . | 
99
4-44. Reversing the Door swing

## Slide 100
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 7. With the freezer door sitting on the bottom hinge, slowly pull the bottom hinge to remove it from the holder on the bottom of the refrigerator. Once the bottom hinge is removed from the holder, remove it from the freezer door, and then pull the freezer door down to remove it from the middle hinge. * CAUTION To prevent the freezer door from falling, make sure to hold the freezer door tight until it is safely removed from the middle hinge. | 
 | 8. Use a Phillips screwdriver and socket wrench (10 mm) to remove the screws fastening the middle hinge. | 
 | 9. Remove the middle hinge screw covers, and then use a Phillips screwdriver to remove the screw. | 
100
4-44. Reversing the Door swing

## Slide 101
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 10. On the opposite side, use a Phillips screwdriver to fasten the screw, and then put on the middle hinge screw covers. | 
 | 11. Remove the bottom hinge screw cover and put it on the opposite side. | 
101
4-44. Reversing the Door swing

## Slide 102
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 12. Disassemble the bottom hinge and reverse all the parts. a. Use a Phillips screwdriver to remove the screw fastening the fixer to the plate. b. Use a spanner (10 mm) to remove the nut and washer fastening the shaft. c. Flip the plate, fasten the fixer with the screw, and then fasten the shaft to the washer and the nut. * CAUTION Make sure the washer is in the correct place. If the shaft is fastened without the washer, the freezer door may fall and cause injury. | 
 | 13. Put the bottom hinge on the holder at the opposite side of where it was removed. | 
102
4-44. Reversing the Door swing

## Slide 103
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 14. On the bottom of the freezer door, remove the door stopper and put it on the opposite side of the door. a. Use a Phillips screwdriver to remove and tighten the screw fastening the door stopper. b. Flip the door stopper before putting it on the opposite side. | 
 | 15. On the top of the freezer door, switch the position of the grommet and the grommet cover. | 
 | 16. Fasten the middle hinge to the opposite side of where it was removed. - Use a Phillips screwdriver and socket wrench (10 mm) to fasten the screws. | 
103
4-44. Reversing the Door swing

## Slide 104
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 17. Attach the freezer door. First, put the freezer door on the bottom hinge, and then push it down to insert the middle hinge shaft into the grommet on top of the freezer door. * CAUTION Do not push the door too hard. Make sure the bottom hinge stays on the holder at the bottom of the refrigerator throughout this step. | 
 | 18. Use a socket wrench to fasten the bottom hinge with the screws. | 
104
4-44. Reversing the Door swing

## Slide 105
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 19. On the bottom of the fridge door, use a Phillips screwdriver to remove the screws. 20. Remove the auto closer, grommet, and door stopper on one side, and the bottom fridge door cover on the other side. | 
 | 21. Put the door stopper, grommet, and auto closer on the opposite side to where they were removed. - Fasten the door stopper and auto closer with the screws using a Phillips screwdriver. 22. Put the bottom fridge door cover on the opposite side to where it was removed. Then, fasten it with the screw using a Phillips screwdriver. | 
105
4-44. Reversing the Door swing

## Slide 106
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 23. On the top of the fridge door, remove the wire cover. - Gently lift either side of the wire cover and pull to remove it from the door. 24. Remove the top-right hinge cover and the top-left door cover. | 
 | 25. Remove the top hinge from the fridge door. | 
 | 26. Use a spanner (11 mm) to remove the shaft and the washer from the plate. 27. Flip the plate, and reattach the washer and the shaft. | 
106
4-44. Reversing the Door swing

## Slide 107
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 28. Remove the grommet and put it on the opposite side. | 
 | 29. Put the top hinge on the opposite side to where it was removed. | 
 | 30. Put the fridge door on the middle hinge. * CAUTION To prevent the fridge door from falling, make sure to hold it tight until the top hinge is fastened. | 
107
4-44. Reversing the Door swing

## Slide 108
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 31. Fasten the top hinge with the screws using a socket wrench (10 mm). | 
 | 32. Remove the space cover from the top cover and then put it on the opposite side. | 
 | 33. Underneath the top cover, pull the wire connector from the holders, and move it to the holders on the opposite side. | 
108
4-44. Reversing the Door swing

## Slide 109
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 34. Move the wire connector on the fridge door to the opposite side. | 
 | 35. Connect the wire connectors from the fridge door and the top cover. | 
 | 36. Put the provided top-left hinge cover on the top cover and place the wires and covers into it. | 
109
4-44. Reversing the Door swing

## Slide 110
4. Disassembly and Assembly
To do list
Part name | How to do | Descriptive Picture
Reversing Door | 37. With the fridge door closed, put the top cover back and fasten it with the screws using a Phillips screwdriver. | 
 | 38. Put the top-left door cover on the opposite side of the door hinge. | 
 | 39. Place the wire from the fridge door into the gap on top of the fridge door. 40.Put the wire cover back onto the fridge door. 41. Open and close the fridge door a few times to check for any problems. | 
110
4-44. Reversing the Door swing

## Slide 111
5. Self Diagnosis & Trouble Shooting
5-1-1. Test Function (Forced Operation / Forced Defrost)
[RB38T* / RB36T* / RB34T*/ RL38T* / RL36T* / RL34T* models]
1. When pressing the “<" and the “>" buttons on the PANEL PCB at the same time for more than 6 seconds, the PANEL DISPLAY will be on and off with an interval of 0.5 second for about 6 seconds. At this time, release the “<" and the “>" buttons, and press the “>" button. Then, it will go into the TEST MODE.
[RB38A* / RB34A* / RL38A* / RL34A* models]
1. When pressing the “<" and the “>" buttons on the PANEL PCB at the same time for more than 6 seconds, the PANEL DISPLAY will be on and off with an interval of 0.5 second for about 6 seconds. At this time, release the “<" and the “>" buttons, and press the “>" button. Then, number ‘1’ will blink. At this time, press the ‘O’ button. it will go into the TEST MODE.
2. At the Test mode, all the display buttons will work as the Test button.
3. Each time the Test button is pressed, it will change in the following order. Forced Operation → Forced F-Defrost → Cancellation (Normal Operation)
4. It is recommended that the unit be re-plugged in to terminate the operation of the Test function.
1) Test Mode Entering Process
5-1. Check-List before Trouble-Shooting
① Press the “<" and the “>" buttons at the same time for 6 seconds.
② When all LEDs are blinking, press the “>" button once.
[RB38T* / RB36T* / RB34T*/ RL38T* / RL36T* / RL34T* models]
[RB38A* / RB34A* / RL38A* / RL34A* models]
① Press the “<" and the “>" buttons at the same time for 6 seconds.
② When all LEDs are blinking, press the “>" button once.
Then, number ‘1’ will blink. At this time, press the ‘O’ button.
This document cannot be used without Samsung's authorization

## Slide 112
5. Self Diagnosis & Trouble Shooting
5-1-1. Test Function (Forced Operation / Forced Defrost)
5-1. Check-List before Trouble-Shooting
This document cannot be used without Samsung's authorization
※ Knob Control Model Only
1. Repeating 3 times : ‘5(Coldest)＇2sec <-> ‘Dead Zone’ 2sec
‘5’ 2sec -> ‘Dead zone’ 2 sec -> ‘5’ 2sec -> ‘Dead zone’ 2 sec ->
‘5’ 2sec -> ‘Dead zone’ 2 sec ...
2. Forced Operation --> Forced F defrost --> Normal operation
TEST feature is changed as this sequence to forced operation.
Coldest
Dead Zone

## Slide 113
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
1-1) When any button is pressed once during the Test Mode, it will enter the Forced Operation. When it starts the Forced Operation, the LED Lamps indicating the Freezer Temperatures (“FF”) will be on showing that it is on the Forced Operation. At this time, it starts alarming with “Beep” sounds.
1-2) When the Forced Operation is selected, the compressor starts without a 7-minute delay in any operation mode. At this time, when it is in a Defrost mode, it stops defrosting and the Forced Operation begins. (If the Forced Operation begins as soon as the compressor stops, it may cause the overload. So, take care when entering into the Forced Operation.)
2) Test Mode Description
1. Forced Operation Function
1-3) When the Forced Operation is selected, the compressor and the F-Fan operate for 24 hours without stopping.
1-4) When the unit is shifted to the Forced Operation, the Freezer and the Fridge temperatures will be automatically set to -23℃ and 1℃ respectively.
1-5) When the Forced Operation is selected, the Power Freeze function won't work. (All the buttons will operate normally.) And, when the Power Freeze function is selected, the Power Freeze LED will go off in 10 seconds.
1-6) When the Forced Defrost or Test Cancellation Mode is selected within a minute with the Forced Operation being selected, the set temperature will be changed to the previously set operating temperature.
1-7) The alarm sound during the Forced Operation keeps on until the Forced Operation completes and there is no cancellation function.
This document cannot be used without Samsung's authorization

## Slide 114
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
2) Test Mode Description
[Twin Cooling models only : RB38A***A** / RB38A***B** / RB38A***3**]
This document cannot be used without Samsung's authorization

## Slide 115
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
2-1) When it is on the Forced Operation during the Test Mode “FF A”, press any button once. Then, the Forced Operation will stop immediately and it will go into the Forced R-Defrost. When it enters the Forced R-Defrost, it indicates that it is on the Forced R-Defrost mode by turning on “rd” on the Freezer Display Panel.
2-2) At this time, it sends out "Beeping" sound for 3 seconds. This alarm sound repeats 0.75 sec On and 0.25 sec Off which keeps on until the Forced R-Defrost finishes.
2) Test Mode Description
2. Forced Defrost Function (R-Defrost)
[Twin Cooling models only : RB38A***A** / RB38A***B** / RB38A***3**]
This document cannot be used without Samsung's authorization

## Slide 116
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
3-1) When it is on the Forced Operation during the Test Mode, press any button once. Then, the Forced Operation will stop immediately and it will go into the Forced F-Defrost. When it enters the Forced F-Defrost, it indicates that it is on the Forced F-Defrost mode by turning on “Fd” on the Freezer Display Panel.
3-2) At this time, it sends out "Beeping" sound for 3 seconds. This alarm sound repeats 0.75 sec On and 0.25 sec Off which keeps on until the Forced F-Defrost finishes.
2) Test Mode Description
3. Forced Defrost Function (F-Defrost)
4-1) When turning the display panel into the Test mode and pressing the TEST button once more during the Forced F-Defrost, the Forced F-Defrost will be cancelled and it will go back to the normal operation. Also, when the unit is plugged out and in again, the Test mode is to be deactivated.
4. Test Cancellation Mode
This document cannot be used without Samsung's authorization

## Slide 117
5. Self Diagnosis & Trouble Shooting
5-1-2. Self-Diagnosis Function
5-1. Check-List before Trouble-Shooting
1-1) When the unit is plugged into the power, MICOM diagnoses the status of the temperature sensors in a few minutes.
1-2) If defective sensor is found after Self-Diagnosis, relevant Display LEDs will blink at an interval of 0.5 sec. and there will be no beeping sound. (Refer to the Self-Diagnosis Check List)
1-3) When there is a defective sensor found and its relevant LED blinks, it will only recognize the Self- Diagnosis button combination and it doesn't do the normal display. But, the temperature will be controlled with the Emergency Operation.
1-4) To cancel the error code, fix the failure of the defective sensor or cancel the Initial Self-Diagnosis Function by pressing the “<“ and the “>” buttons for 12 seconds.
1) Self-Diagnosis Function upon Initial Power-On
This document cannot be used without Samsung's authorization

## Slide 118
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
2-1) During the Normal Operation, press the “<“ + “>” buttons for 12 seconds.
It will send out a "Ding-Dong" buzzer sound and go into the Self Diagnosis Function.
2-2) When it goes into the Self-Diagnosis, the entire display panel goes off and when there is an
error occurred, it will last for 60 seconds continuously and go to the normal operation whether
or not the error is fixed. (It sends out "Ding-Dong" sound)
2-3) Buttons won't work during Self-Diagnosis.
2) Self-Diagnosis Function during Normal Operation
[RB38T* / RB36T* / RB34T*/ RL38T* / RL36T* / RL34T* models]
[RB38A* / RB34A* / RL38A* / RL34A* models]
2-1) During the Normal Operation, Press the “<" and the “>" buttons at the same time for 6 seconds.
and then, When all LEDs are blinking, press the “>" button once. Then, number ‘1’ will blink.
At this time, press the ‘>’ button until the number ‘3’ blinks. At this time, press the ‘O’ button.
2-2) When it goes into the Self-Diagnosis, the entire display panel goes off and when there is an
error occurred, it will last for 60 seconds continuously and go to the normal operation whether
or not the error is fixed. (It sends out "Ding-Dong" sound)
2-3) Buttons won't work during Self-Diagnosis.
This document cannot be used without Samsung's authorization

## Slide 119
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
* Self-diagnosis CHECK LIST
NO | List | Freezer | Fridge | Details
1 | F Sensor | 1 | C | OPEN/SHORT
2 | R Sensor | 2 |  | OPEN/SHORT
3 | F Defrost Sensor | 4 |  | OPEN/SHORT
4 | R Defrost Sensor | 5 |  | OPEN/SHORT
5 | EXT Sensor | 6 |  | OPEN/SHORT
6 | Humidity Sensor | 13 |  | OPEN/SHORT
7 | F Fan Error | 21 |  | F-FAN Error
8 | R Fan Error | 22 |  | R-FAN Error
9 | C Fan Error | 23 |  | C-FAN Error
10 | Defrost Error | 24 |  | Defrosting ended due to max time
11 | Display Comm Error | 41 |  | Display Communication Error
12 | Comp Comm Error | 44 |  | Comp Communication Error
13 | WIFI Comm Error (WIFI model Only) | 52 |  | WIFI Communication Error
14 | F Abnormal High Temp Error | 71 |  | F Abnormal High Temp Error
15 | R Abnormal High Temp Error | 72 |  | R Abnormal High Temp Error
16 | Comp run fail Error | 81 |  | Comp run fail Error
17 | Comp IPM Fault Error | 82 |  | Comp IPM Fault Error
18 | Comp Abnoraml Current error | 83 |  | Comp Abnoraml Current error
19 | Comp Motor constraint error | 84 |  | Comp Motor constraint error
20 | Comp Low Volt Error | 85 |  | Comp Low Volt Error
21 | Comp High Volt Error | 86 |  | Comp High Volt Error
22 | Comp IPM Shut Down | 96 |  | Comp IPM Shut Down Error
This document cannot be used without Samsung's authorization

## Slide 120
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
* Self-diagnosis CHECK LIST
NO | List | LED Blink | Details
0 | F Sensor | 1 Time | Open/Short
1 | F Defrost Sensor | 2 Times | Open/Short
2 | EXT Sensor | 3 Times | Open/Short
3 | Defrost Error | 5 Times | Defrosting ended due to max time
4 | R Sensor | 6 Times | Open/Short
5 | Knob Switch Error | 9 Times | Open/Short
6 | Comp Error | 10 Times | Comp run fail Error
 |  |  | Comp IPM Fault Error
 |  |  | Comp Abnoraml Current error
 |  |  | Comp Motor constraint error
 |  |  | Comp Low Volt Error
 |  |  | Comp High Volt Error
 |  |  | Comp IPM Shutdown Error
7 | F Fan Error | 11 Times | F-FAN Error
8 | Comp Comm Error | 14 Times | Inverter Comm Error
9 | Model Option Error | 15 Times | EEPROM option value is not written
This document cannot be used without Samsung's authorization
※ Knob Control Model Only
: When an error occurs, Error-LED in PBA blinks.

## Slide 121
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 122
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 123
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 124
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 125
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 126
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
This document cannot be used without Samsung's authorization
5-1. Check-List before Trouble-Shooting (Twin / Bespoke Mono C,D)

## Slide 127
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
5-1. Check-List before Trouble-Shooting (Mono C,D,E,F / Bespoke Mono E,F)

## Slide 128
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
5-1. Check-List before Trouble-Shooting (Mono C,D,E,F / Bespoke Mono E,F)

## Slide 129
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
5-1. Check-List before Trouble-Shooting (Mono C,D,E,F / Bespoke Mono E,F)

## Slide 130
5. Self Diagnosis & Trouble Shooting
* Self-diagnosis CHECK LIST
5-1. Check-List before Trouble-Shooting (Mono C,D,E,F / Bespoke Mono E,F)

## Slide 131
5. Self Diagnosis & Trouble Shooting
5-1-3. Load Status Display Function
1) When pressing the “<" and the “O" buttons on the PANEL PCB at the same time for more than 6 seconds, the PANEL DISPLAY will be on and off with an interval of 0.5 second for about 6 seconds. At this time, release the “<" and the “O" buttons, and press the “>" button. Then, it will go into the Load Display mode.
[RB38T* / RB36T* / RB34T*/ RL38T* / RL36T* / RL34T* models]
[RB38A* / RB34A* / RL38A* / RL34A* models]
2) The Load Display function shows what MICOM signals come out from MAIN PCB. But, it just indicates that there are MICOM signals coming out. It does not necessarily mean that the related parts (Loads) are operating. In other word, even though it shows a certain load working, the related part may not operate due to such as a defective PCB relay or the defective part itself (it needs checking).
3) The Load Display function lasts for 30 seconds and then it goes back to the normal operation.
4) The following image shows load locations with the LEDs.
1) During the Normal Operation, Press the “<" and the “>" buttons at the same time for 6 seconds. and then, When all LEDs are blinking, press the “>" button once. Then, number ‘1’ will blink. At this time, press the ‘>’ button until the number ‘7’ blinks. At this time, press the ‘O’ button.
5-1. Check-List before Trouble-Shooting
This document cannot be used without Samsung's authorization

## Slide 132
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
* Load mode Check list
This document cannot be used without Samsung's authorization

## Slide 133
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
* Load mode Check list
[Twin Cooling models only : RB38A***A** / RB38A***B** / RB38A***3**]
This document cannot be used without Samsung's authorization

## Slide 134
5-1-4. Restoration of Previous Settings upon Instant Power Outage
1) If the Display Panel is initialized by the instant power outage, it will cause customer inquiries. To prevent this, when the power is restored, the previous settings will be restored or reset based on the inside temperature of the Freezer Compartment.
2) Upon the initial power on, it checks its Freezer temperature. When it is lower than +10℃, it is to be considered as an instant power failure and it brings back all its previous operation functions (such as Power Freeze, Vacation, Fridge, Freezer, etc) related to the panel display.
3) When it is higher than +10℃, it is to be considered as a long-period power failure and it will initialize the panel display. (Freezer : Automatically set to -19℃, Fridge : Automatically set to 3℃)
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
This document cannot be used without Samsung's authorization

## Slide 135
5-1-5. Demo Mode Function for Store Display
When pressing the “<" and the “>" buttons on the PANEL PCB at the same time for more than 6 seconds, the PANEL DISPLAY will be on and off with an interval of 0.5 second for about 6 seconds. At this time, release the “<" and the “>" buttons, and press the “O" button. Then, it will go into the Demo mode.
When the unit is in Demo Mode, all the functions including the Display Panel works normal. But, the Compressor does not operate.
3) To cancel the Demo Mode, press the same buttons as you enter into the Demo Mode or turn off its power.
4) Also, when the Freezer or Fridge room temperature goes over 65℃ during the Demo Mode, it will go back to the normal cooling operation.
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
① Press the “<“ + “>” buttons for 6 seconds at the same time. Then, the Display LEDs will blink for 6 seconds. At this time, release the buttons
② and, press the “O” button once.
This document cannot be used without Samsung's authorization

## Slide 136
5-1-6. Option Setting Function
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
1) During the Normal Operation, Press the “<“ + “O” buttons for 6 seconds at the same time. Then, the Display LEDs will blink for 6 seconds. At this time, release the buttons and, press the “<” button once. It will send out a "Ding-Dong" buzzer sound and go into the Option Setting mode.
①
②
[RB38T* / RB36T* / RB34T*/ RL38T* / RL36T* / RL34T* models]
[RB38A* / RB34A* / RL38A* / RL34A* models]
1) During the Normal Operation, Press the “<" and the “>" buttons at the same time for 6 seconds. and then, When all LEDs are blinking, press the “>" button once. Then, number ‘1’ will blink. At this time, press the ‘>’ button until the number ‘9’ blinks. At this time, press the ‘O’ button.
①
②
When there is no button press for 20 seconds at the Option Setting Mode, it will go back to the normal display mode.
This document cannot be used without Samsung's authorization

## Slide 137
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
Option Mode & Button Control Description
① It shows the chosen option's number.
② It shows the chosen option's setting value.
③ It increases the option number.
④ It decreases the option number.
⑤ It increases the value of the option by one step. (The value rotates.)
①
②
③
④
⑤
This document cannot be used without Samsung's authorization

## Slide 138
● In this mode the whole display will get turned off except for the following adjustment:
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
1) For example, if you want to adjust the option and shift the standard temperature of the Freezer by -2℃, do as follows. This function is to change the standard temperature. If the current standard temperature is -21 ℃ for the Freezer, and if you decrease it by 2 ℃ by using the option, the standard temperature will be -23 ℃. That is, if you change the temperature option, even if it is set to be -21 ℃ on the Panel, the operation will be performed with -23 ℃ as the standard inside. Therefore, it means that the standard temperature is controlled to be lower by 2 ℃ than the temperature set on the Panel.
Note
When the product is released, all data are cleared in the option function. That is, the product is released with the set value as "0". However, some set values may be changed during mass-production for the purpose of improvement of quality. Thus, please always check the Quality Information, etc.
This document cannot be used without Samsung's authorization

## Slide 139
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
2) When you change into the Option Mode, the display panel will be in the status for the option number and the set value to mean "0." (Though the product should be released with '0' for the Freezer and '0' for the Fridge, the default value may be changed for the purpose of improvement of quality during mass-production.)
- When only '0' is turned ON for the Fridge, the Freezer Temperature Option Item will be set, and the current Freezer temperature set value will be displayed on the Freezer Temperature Display.
3) If you adjust the option number of the Fridge to be "0" and sets "4" as in the below Freezer Option Table, the Freezer standard temperature will be lowered by 2℃. (Refer to the Freezer temperature change picture.) : If you wait for 20 seconds after the adjustment is completed, the Micom will save the set value in the EEPROM, and the product will return to the normal display and the Option Setting Mode will be canceled.
4) You can adjust the Fridge temperature following the same method as above.
5) When the product is released from the factory, the option function is set at the EERPOM. Therefore, please do not modify the product unless you are in a special case. The option function's setting is completed only when it returns to the normal Display in 20 seconds. Therefore, do not turn the power OFF before it returns to the normal Display.
This document cannot be used without Samsung's authorization

## Slide 140
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
5-1-7. Option Table
1) Freezer Temp Shift Table
Note
There are other option setting functions. But, it's got to do with the performance of the unit, not for repair purposes. So, they are not handled in this manual. (Except those described in this manual, do not change other values)
Setting Item | Freezer Temp Shift
Option Item | Location : Fridge Temp LED
 | 0
Setting Value | Option Value
Freezer Temp | 
0 | 0℃
1 | -0.5℃
2 | -1.0℃
3 | -1.5℃
4 | -2.0℃
5 | -2.5℃
6 | -3.0℃
7 | -3.5℃
8 | +0.5℃
9 | +1.0℃
10 | +1.5℃
11 | +2.0℃
12 | +2.5℃
13 | +3.0℃
14 | +3.5℃
15 | +4.0℃
Ex) When shifting the Freezer default temp by -2.0℃
This document cannot be used without Samsung's authorization

## Slide 141
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
5-1-7. Option Table
2) Fridge Temp Shift Table
Setting Item | Fridge Temp Shift
Option Item | Location : Fridge Temp Display
 | 1
Setting Value | Option Value
Fridge Temp Displa Panel Set Value | 
0 | 0℃
1 | -0.5℃
2 | -1.0℃
3 | -1.5℃
4 | -2.0℃
5 | -2.5℃
6 | -3.0℃
7 | -3.5℃
8 | +0.5℃
9 | +1.0℃
10 | +1.5℃
11 | +2.0℃
12 | +2.5℃
13 | +3.0℃
14 | +3.5℃
15 | +4.0℃
Ex) When shifting the Fridge default temp by +2.0℃
This document cannot be used without Samsung's authorization

## Slide 142
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
5-1-7. Option Table
3) Display On/Off Table
Setting Item | Fridge Temp Shift
Option Item | Location : Fridge Temp Display
 | 16
Setting Value | Option Value
Fridge Temp Displa Panel Set Value | 
0 | Display Off in 10 seconds after feeding the Key value
1 | Display On mode persists
2 | Display On mode persists
Ex) When set Fridge Value “1”
This document cannot be used without Samsung's authorization

## Slide 143
5. Self Diagnosis & Trouble Shooting
5-1. Check-List before Trouble-Shooting
5-1-7. Option Table
[Twin Cooling models only : RB38A***A** / RB38A***B** / RB38A***3**]
4) Freezer Convert (SoftFreeze/Chill/Fridge) Temp Shift Table
Setting Item | Fridge Temp Shift
Option Item | Location : Fridge Temp Display
 | 31
Ex) When shifting the Freezer Convert Function temp by +0.5℃
This document cannot be used without Samsung's authorization

## Slide 144
℃ | ℉ | Voltage | Ω | ℃ | ℉ | Voltage | Ω
-50 | -58 | 4.694 | 153319 | -36 | -32.8 | 4.385 | 71246
-49 | -56.2 | 4.677 | 144794 | -35 | -31 | 4.356 | 67634
-48 | -54.4 | 4.659 | 136798 | -34 | -29.2 | 4.326 | 64227
-47 | -52.6 | 4.641 | 129294 | -33 | -27.4 | 4.296 | 61012
-46 | -50.8 | 4.622 | 122248 | -32 | -25.6 | 4.264 | 57977
-45 | -49 | 4.602 | 115631 | -31 | -23.8 | 4.232 | 55112
-44 | -47.2 | 4.581 | 109413 | -30 | -22 | 4.199 | 52406
-43 | -45.4 | 4.560 | 103569 | -29 | -20.2 | 4.165 | 49848
-42 | -43.6 | 4.537 | 98073 | -28 | -18.4 | 4.129 | 47431
-41 | -41.8 | 4.514 | 92903 | -27 | -16.6 | 4.093 | 45146
-40 | -40 | 4.490 | 88037 | -26 | -14.8 | 4.056 | 42984
-39 | -38.2 | 4.465 | 83456 | -25 | -13 | 4.018 | 40938
-38 | -36.4 | 4.439 | 79142 | -24 | -11.2 | 3.980 | 39002
-37 | -34.6 | 4.412 | 75077 | -23 | -9.4 | 3.940 | 37169
DATA1.Temp Table
Conversion Table - Temperature/MICOM PORT Voltage/Resistance
SENSOR CHIP : PX41C
To do list
5. Self Diagnosis & Trouble Shooting
5-2. Troubleshooting Flow-Chart by Symptoms
This document cannot be used without Samsung's authorization

## Slide 145
℃ | ℉ | Voltage | Ω | ℃ | ℉ | Voltage | Ω
-22 | -7.6 | 3.899 | 35433 | -5 | 23 | 3.107 | 16419
-21 | -5.8 | 3.858 | 33788 | -4 | 24.8 | 3.057 | 15731
-20 | -4 | 3.816 | 32230 | -3 | 26.6 | 3.006 | 15076
-19 | -2.2 | 3.773 | 30752 | -2 | 28.4 | 2.955 | 14452
-18 | -0.4 | 3.729 | 29350 | -1 | 30.2 | 2.904 | 13857
-17 | 1.4 | 3.685 | 28021 | 0 | 32 | 2.853 | 13290
-16 | 3.2 | 3.640 | 26760 | 1 | 33.8 | 2.802 | 12749
-15 | 5 | 3.594 | 25562 | 2 | 35.6 | 2.751 | 12233
-14 | 6.8 | 3.548 | 24425 | 3 | 37.4 | 2.700 | 11741
-13 | 8.6 | 3.501 | 23345 | 4 | 39.2 | 2.649 | 11271
-12 | 10.4 | 3.453 | 22320 | 5 | 41 | 2.599 | 10823
-11 | 12.2 | 3.405 | 21345 | 6 | 42.8 | 2.548 | 10395
-10 | 14 | 3.356 | 20418 | 7 | 44.6 | 2.498 | 9986
-9 | 15.8 | 3.307 | 19537 | 8 | 46.4 | 2.449 | 9596
-8 | 17.6 | 3.258 | 18698 | 9 | 48.2 | 2.399 | 9223
-7 | 19.4 | 3.208 | 17901 | 10 | 50 | 2.350 | 8867
-6 | 21.2 | 3.158 | 17142 | 11 | 51.8 | 2.301 | 8526
To do list
5. Self Diagnosis & Trouble Shooting
5-2. Troubleshooting Flow-Chart by Symptoms
This document cannot be used without Samsung's authorization

## Slide 146
℃ | ℉ | Voltage | Ω | ℃ | ℉ | Voltage | Ω
12 | 53.6 | 2.253 | 8200 | 29 | 84.2 | 1.520 | 4369
13 | 55.4 | 2.205 | 7888 | 30 | 86 | 1.483 | 4218
14 | 57.2 | 2.158 | 7590 | 31 | 87.8 | 1.447 | 4072
15 | 59 | 2.111 | 7305 | 32 | 89.6 | 1.412 | 3933
16 | 60.8 | 2.064 | 7032 | 33 | 91.4 | 1.377 | 3799
17 | 62.6 | 2.019 | 6771 | 34 | 93.2 | 1.343 | 3670
18 | 64.4 | 1.974 | 6521 | 35 | 95 | 1.309 | 3547
19 | 66.2 | 1.929 | 6281 | 36 | 96.8 | 1.277 | 3428
20 | 68 | 1.885 | 6052 | 37 | 98.6 | 1.253 | 3344
21 | 69.8 | 1.842 | 5832 | 38 | 100.4 | 1.213 | 3204
22 | 71.6 | 1.799 | 5621 | 39 | 102.2 | 1.183 | 3098
23 | 73.4 | 1.757 | 5419 | 40 | 104 | 1.153 | 2997
24 | 75.2 | 1.716 | 5225 | 41 | 105.8 | 1.124 | 2899
25 | 77 | 1.675 | 5039 | 42 | 107.6 | 1.095 | 2805
26 | 78.8 | 1.636 | 4861 | 43 | 109.4 | 1.068 | 2714
27 | 80.6 | 1.596 | 4690 | 44 | 111.2 | 1.040 | 2627
28 | 82.4 | 1.558 | 4526 | 45 | 113 | 1.014 | 2543
To do list
5. Self Diagnosis & Trouble Shooting
5-2. Troubleshooting Flow-Chart by Symptoms
This document cannot be used without Samsung's authorization

## Slide 147
℃ | ℉ | Voltage | Ω | ℃ | ℉ | Voltage | Ω
46 | 114.8 | 0.988 | 2462 | 66 | 150.8 | 0.598 | 1335
47 | 116.6 | 0.963 | 2384 | 67 | 152.6 | 0.574 | 1297
48 | 118.4 | 0.938 | 2309 | 68 | 154.4 | 0.560 | 1260
49 | 120.2 | 0.914 | 2237 | 69 | 156.2 | 0.546 | 1225
50 | 122 | 0.891 | 2167 | 70 | 158 | 0.532 | 1190
51 | 123.8 | 0.868 | 2100 | 71 | 159.8 | 0.519 | 1157
52 | 125.6 | 0.846 | 2036 | 72 | 161.6 | 0.506 | 1125
53 | 127.4 | 0.824 | 1973 | 73 | 163.4 | 0.493 | 1093
54 | 129.2 | 0.803 | 1913 | 74 | 165.2 | 0.481 | 1063
55 | 131 | 0.783 | 1855 | 75 | 167 | 0.469 | 1034
56 | 132.8 | 0.762 | 1799 | 76 | 168.8 | 0.457 | 1006
57 | 134.6 | 0.743 | 1745 | 77 | 170.6 | 0.446 | 978
58 | 136.4 | 0.724 | 1693 | 78 | 172.4 | 0.435 | 952
59 | 138.2 | 0.706 | 1642 | 79 | 174.2 | 0.424 | 926
60 | 140 | 0.688 | 1594 | 80 | 176 | 0.414 | 902
61 | 141.8 | 0.670 | 1547 | 81 | 177.8 | 0.404 | 877
62 | 143.6 | 0.653 | 1502 | 82 | 179.6 | 0.394 | 854
63 | 145.4 | 0.636 | 1458 | 83 | 181.4 | 0.384 | 832
64 | 147.2 | 0.620 | 1416 | 84 | 183.2 | 0.375 | 810
65 | 149 | 0.604 | 1375 |  |  |  | 
To do list
5. Self Diagnosis & Trouble Shooting
5-2. Troubleshooting Flow-Chart by Symptoms
This document cannot be used without Samsung's authorization

## Slide 148
5-2-1. When Self-Diagnosis Error occurs
5. Self Diagnosis & Trouble Shooting
- The Display Panel shows the Sensor Error and, when the unit is plugged in and there are sensor errors, the unit does not operate and LED related to the defective sensors keep blinking.
- When sensor defects occur during the operation, the unit keeps working. But, it shifts to the Emergency Operation and it may not work properly. So, please check the unit according to the Self Diagnosis function.
1) When the R-Sensor is defective (Twin / Bespoke Mono C,D)
ERROR CODE
Start
MAIN PCB Connector CN1 is
inserted properly?
R Sensor is
normal?
YES
Connector contact defect / Reconnect
NO
YES
Replace Temp Sensor
NO
DATA1.Temp Table
** Sensor Resistance Reading Location ** R : Between CN30 #13 and #15 ** 0Ω : Short / ∞Ω : Open
This document cannot be used without Samsung's authorization

## Slide 149
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
YES
Voltage between MAIN PCB
Connector CN30-“13"(ORG)
and CN1-“15"(GRY)?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
Sensor MICOM/Connector # | 
R | Between Connector CN30- “13"(ORG) and CN1-“15"(GRY)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
Input Voltage at MIC01
MICOM Pin #7 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at MIC01 MICOM #7 is the same as the value between CN30-“13"(ORG) and CN30-“15"(GRY)
PCB and Temp Sensor are normal.
Check the connector contact.
This document cannot be used without Samsung's authorization

## Slide 150
5-2-1. When Self-Diagnosis Error occurs
5. Self Diagnosis & Trouble Shooting
- The Display Panel shows the Sensor Error and, when the unit is plugged in and there are sensor errors, the unit does not operate and LED related to the defective sensors keep blinking.
- When sensor defects occur during the operation, the unit keeps working. But, it shifts to the Emergency Operation and it may not work properly. So, please check the unit according to the Self Diagnosis function.
1) When the R-Sensor is defective (Mono C,D,E,F / Bespoke Mono E,F)
ERROR CODE
Start
MAIN PCB Connector CN30 is
inserted properly?
R Sensor is
normal?
YES
Connector contact defect / Reconnect
NO
YES
Replace Temp Sensor
NO
DATA1.Temp Table
** Sensor Resistance Reading Location ** R : Between CN30 #13 and #15 ** 0Ω : Short / ∞Ω : Open
This document cannot be used without Samsung's authorization

## Slide 151
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
YES
Voltage between MAIN PCB
Connector CN30-“13"(ORG)
and CN30-“15"(GRY)?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
Sensor MICOM/Connector # | 
R | Between Connector CN30- “13"(ORG) and CN30-“15"(GRY)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
Input Voltage at MIC01
MICOM Pin #8 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at MIC01 MICOM #8 is the same as the value between CN30-“13"(ORG) and CN30-“15"(GRY)
PCB and Temp Sensor are normal.
Check the connector contact.
This document cannot be used without Samsung's authorization

## Slide 152
5. Self Diagnosis & Trouble Shooting
2) When the EXT Sensor is defective (Twin / Bespoke Mono C,D)
5-2-1. When Self-Diagnosis Error occurs
Start
MAIN PCB SENSOR
(CN1) is inserted properly?
EXT Sensor is
normal?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between
MAIN PCB Connector CN1-“9"and“11"
Check the assembled status of the Sensor.
NO (0.6V>Value or Value>4.6V)
DATA1.Temp Table
** Sensor Resistance Reading Location ** Ambient : Between CN1 #9 and #11. ** Located in the PCB Box ** 0Ω : Short / ∞Ω : Open
Sensor MICOM/Connector # | 
Ambient | Between Connector CN1- “9"and CN1-“11"
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
ERROR CODE
YES

## Slide 153
5. Self Diagnosis & Trouble Shooting
2) When the EXT-Sensor is defective
5-2-1. When Self-Diagnosis Error occurs
YES
Input Voltage at MIC01
MICOM Pin #2 is normal?
YES
NO
Check Soldering Defect & Short
Voltage at MIC01 MICOM #2 is the same as the value between CN1-“9"(S/BLU) and CN1-“11"(W/GRY) of the CN1 on MAIN PBA.
PCB and Temp Sensor are normal.
Check the connector contact.

## Slide 154
5. Self Diagnosis & Trouble Shooting
2) When the EXT Sensor is defective (Mono C,D,E,F / Bespoke Mono E,F)
5-2-1. When Self-Diagnosis Error occurs
Start
MAIN PCB SENSOR
(CN31) is inserted properly?
EXT Sensor is
normal?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between
MAIN PCB Connector CN30-“5"(S/BLU) and
CN30-“7"(W/GRY)?
Check the assembled status of the Sensor.
NO (0.6V>Value or Value>4.6V)
DATA1.Temp Table
** Sensor Resistance Reading Location ** Ambient : Between CN30 #5 and #7. ** Located in the PCB Box ** 0Ω : Short / ∞Ω : Open
Sensor MICOM/Connector # | 
Ambient | Between Connector CN30- “5"(S/BLU) and CN30-“7"(W/GRY)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
ERROR CODE
YES
This document cannot be used without Samsung's authorization

## Slide 155
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
YES
Input Voltage at MIC01
MICOM Pin #3 is normal?
YES
NO
Check Soldering Defect & Short
Voltage at MIC01 MICOM #3 is the same as the value between CN30-“5"(S/BLU) and CN30-“7"(W/GRY) of the CN30 on MAIN PBA.
PCB and Temp Sensor are normal.
Check the connector contact.
This document cannot be used without Samsung's authorization

## Slide 156
5. Self Diagnosis & Trouble Shooting
3) When the F-Sensor is defective (Twin / Bespoke Mono C,D)
5-2-1. When Self-Diagnosis Error occurs
MAIN PCB Connector
CN1 is inserted properly?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between MAIN PCB
Connector CN1-“13"(ORG)
and CN1-“15"(GRY) is normal?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
** Sensor Resistance Reading Location ** F : Between CN1 #13 and #15 ** 0Ω : Short / ∞Ω : Open
Sensor MICOM/Connector # | 
F | Between Connector CN1- “13"(ORG) and CN30-“15"(GRY)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
F Sensor is
normal?
ERROR CODE
Start
YES

## Slide 157
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
Input Voltage at MIC01
MICOM Pin #8 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at IC10 MICOM # 8 is the same as the value between CN1-“13"(BRN) and CN1-“15"(GRY)
PCB and Temp Sensor are normal.
Check the connector contact.

## Slide 158
5. Self Diagnosis & Trouble Shooting
3) When the F-Sensor is defective (Mono C,D,E,F / Bespoke Mono E,F)
5-2-1. When Self-Diagnosis Error occurs
MAIN PCB Connector
CN30 is inserted properly?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between MAIN PCB
Connector CN30-“13"(ORG)
and CN30-“15"(GRY) is normal?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
** Sensor Resistance Reading Location ** F : Between CN30 #13 and #15 ** 0Ω : Short / ∞Ω : Open
Sensor MICOM/Connector # | 
F | Between Connector CN30- “13"(ORG) and CN30-“15"(GRY)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
F Sensor is
normal?
ERROR CODE
Start
YES
This document cannot be used without Samsung's authorization

## Slide 159
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
Input Voltage at MIC01
MICOM Pin #7 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at IC10 MICOM # 7 is the same as the value between CN30-“13"(BRN) and CN30-“15"(GRY)
PCB and Temp Sensor are normal.
Check the connector contact.
This document cannot be used without Samsung's authorization

## Slide 160
5. Self Diagnosis & Trouble Shooting
4) When the F DEF-Sensor is defective (Twin / Bespoke Mono C,D)
5-2-1. When Self-Diagnosis Error occurs
MAIN PCB Connector
CN1 is inserted properly?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between MAIN PCB
Connector CN1-“8"(PRP) and “7"(PNK)
is normal?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
Sensor MICOM/Connector # | 
F DEF | Between Connector CN1"- “8"(PRP) and CN1-“7"(PNK)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
F-DEF Sensor is
normal?
ERROR CODE
Start
YES
DATA1.Temp Table
** Sensor Resistance Reading Location ** F-DEF : Between CN1 #8 and #7 ** 0Ω : Short / ∞Ω : Open

## Slide 161
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
Input Voltage at MIC01
MICOM Pin #4 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at MIC01 MICOM # 4 is the same as the value between CN1-“8"(PRP) and CN30-“7"(PNK).
PCB and Temp Sensor are normal.
Check the connector contact.

## Slide 162
5. Self Diagnosis & Trouble Shooting
4) When the F DEF-Sensor is defective (Mono C,D,E,F / Bespoke Mono E,F)
5-2-1. When Self-Diagnosis Error occurs
MAIN PCB Connector
CN30 is inserted properly?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between MAIN PCB
Connector CN30-“6"(PRP) and “8"(PNK)
is normal?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
Sensor MICOM/Connector # | 
F DEF | Between Connector CN30"- “6"(PRP) and CN30-“8"(PNK)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
F-DEF Sensor is
normal?
ERROR CODE
Start
YES
DATA1.Temp Table
** Sensor Resistance Reading Location ** F-DEF : Between CN30 #6 and #8 ** 0Ω : Short / ∞Ω : Open
This document cannot be used without Samsung's authorization

## Slide 163
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
Input Voltage at MIC01
MICOM Pin #4 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at MIC01 MICOM # 4 is the same as the value between CN30-“6"(PRP) and CN30-“8"(PNK).
PCB and Temp Sensor are normal.
Check the connector contact.
This document cannot be used without Samsung's authorization

## Slide 164
5. Self Diagnosis & Trouble Shooting
5) When the R DEF-Sensor is defective
5-2-1. When Self-Diagnosis Error occurs
MAIN PCB Connector
CN1 is inserted properly?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between MAIN PCB
Connector CN1-“28"and “22"is normal?
Check the wire connection
NO (0.6V>Value or Value>4.6V)
Sensor MICOM/Connector # | 
R DEF | Between Connector CN1"- “28"(PRP) and CN1-“22"(PNK)
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
R-DEF Sensor is
normal?
ERROR CODE
Start
YES
DATA1.Temp Table
** Sensor Resistance Reading Location ** R-DEF : Between CN1 #28 and #22 ** 0Ω : Short / ∞Ω : Open

## Slide 165
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
Input Voltage at MIC01
MICOM Pin #3 is normal?
YES
NO
Check Soldering Defect & Short
YES
Voltage at MIC01 MICOM # 3 is the same as the value between CN1-“28"(PRP) and CN30-“22"(PNK).
PCB and Temp Sensor are normal.
Check the connector contact.

## Slide 166
5. Self Diagnosis & Trouble Shooting
6) When the Humidity Sensor is defective
5-2-1. When Self-Diagnosis Error occurs
Start
MAIN PCB SENSOR
(CN1) is inserted properly?
Humidity Sensor is
normal?
YES
Connector contact defect /
Reconnect
NO
YES
Replace Temp Sensor
NO
Voltage between
MAIN PCB Connector CN1-“5"and“7"
Check the assembled status of the Sensor.
NO (0.6V>Value or Value>4.6V)
DATA1.Temp Table
** Sensor Resistance Reading Location ** Ambient : Between CN1 #5 and #7. ** Located in the PCB Box ** 0Ω : Short / ∞Ω : Open
Sensor MICOM/Connector # | 
Ambient | Between Connector CN1- “5"and CN1-“7"
Voltage : Between 4.6V ~ 0.6V | 
Refer to Circuit Diagram
ERROR CODE
YES
13

## Slide 167
5. Self Diagnosis & Trouble Shooting
5-2-1. When Self-Diagnosis Error occurs
YES
Input Voltage at MIC01
MICOM Pin #6 is normal?
YES
NO
Check Soldering Defect & Short
Voltage at MIC01 MICOM #6 is the same as the value between CN1-“5" and CN1-“7" of the CN1 on MAIN PBA.
PCB and Temp Sensor are normal.
Check the connector contact.

## Slide 168
5. Self Diagnosis & Trouble Shooting
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor)
The Compressor is Off.
Run Forced Operation
YES
NO
YES
- This refrigerator uses the BLDC Fan Motor.
The BLDC Motor operates with DC 7~12V.
The F-Fan motor generally runs together with the compressor.
☞ When checking with the Self Diagnosis
Start
It reads DC7~12 between
MAIN PCB GND and CN1 #19?
Apply power in 7 minutes after turning the motor off.
(To prevent the compressor from
being overloaded)
Upon the initial power on, the compressor and the F-Fan operate. And, when the Freezer temp is lower than 10℃, it will be regarded as an instant power failure, starting in 7 minutes.
YES
F FAN ERROR
FAN operates.
NO
NO
(Twin / Bespoke Mono C,D)

## Slide 169
5. Self Diagnosis & Trouble Shooting
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor)
YES
NO
YES
Replace MAIN PCB
◆ Possible Causes
① Defective FAN-MOTOR
② Contact problem at the terminal
(MAIN PCB CONNECTOR-TERMINAL (CN1. 17,19, 21), Contact problem at Freezer Fan Motor Connector,
Defective Motor Wire)
③ Check the motor rotating pulse input upon Fan Motor
operation. (Refer to Fan-Motor Circuit in this manual)
repeats DC7~12V or lower
than DC 2V between MAIN PCB GND and CN1 PIN #19 or PIN #21 respectively
(Twin / Bespoke Mono C,D)

## Slide 170
5. Self Diagnosis & Trouble Shooting
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor)
The Compressor is Off.
Run Forced Operation
YES
NO
YES
- This refrigerator uses the BLDC Fan Motor.
The BLDC Motor operates with DC 7~12V.
The F-Fan motor generally runs together with the compressor.
☞ When checking with the Self Diagnosis
Start
It reads DC7~12 between
MAIN PCB GND and CN30 #19?
Apply power in 7 minutes after turning the motor off.
(To prevent the compressor from
being overloaded)
Upon the initial power on, the compressor and the F-Fan operate. And, when the Freezer temp is lower than 10℃, it will be regarded as an instant power failure, starting in 7 minutes.
YES
F FAN ERROR
FAN operates.
NO
NO
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 171
5. Self Diagnosis & Trouble Shooting
5-2-2. When the Freezer Fan does not operate (OPTION, BLDC Motor)
YES
NO
YES
Replace MAIN PCB
◆ Possible Causes
① Defective FAN-MOTOR
② Contact problem at the terminal
(MAIN PCB CONNECTOR-TERMINAL (CN30. 17,19, 21), Contact problem at Freezer Fan Motor Connector,
Defective Motor Wire)
③ Check the motor rotating pulse input upon Fan Motor
operation. (Refer to Fan-Motor Circuit in this manual)
repeats DC7~12V or lower
than DC 2V between MAIN PCB GND and CN30 PIN #19 or PIN #21 respectively
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 172
5. Self Diagnosis & Trouble Shooting
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan)
Start
It reads DC7~12
between MAIN PCB
GND and CN70 #7.
YES
FAN operates.
NO
The Compressor is Off.
Run Forced Operation
YES
NO
- This refrigerator uses the BLDC Fan Motor.
The BLDC Motor operates with DC 7~12V.
- The F-Fan motor generally runs together with the compressor.
☞ When checking with the Self Diagnosis
Apply power in 7 minutes after turning the motor off.
(To prevent the compressor from being overloaded)
NO
Upon the initial power on, the compressor and the C-Fan operate. And, this function starts operating when the compressor is about to run right after an instant power outage.
(Twin / Bespoke Mono C,D)

## Slide 173
5. Self Diagnosis & Trouble Shooting
YES
Replace MAIN PCB
NO
Does it read DC7~12V
(between MAIN PCB GND and CN70 #7) and lower than DC 2V(between MAIN PCB GND and CN70 #8)?
YES
◆Note : C-FAN Operations by Ambient Temperature 1. 29℃ or higher : Turns on after a 10 minute pause when the Compressor starts operating. 2. 18℃~28℃ : Turns on immediately when the Compressor starts operating. 3. 18℃ or higher : Turns off after a minute when the Compressor stops operating. 4. 17℃ or lower : Turns on when the Compressor starts operating. (But, the C-FAN turns on when the C-FAN is detected as bein g ristricted for an hour continually). 5. 17℃ or lower : Turns off (for up to 150 minutes) when the Compressor stops operating.
◆ Possible Causes
① Defective FAN-MOTOR
② Contact problem at the terminal
(MAIN PCB CONNECTOR-TERMINAL (CN70. 6,7,8), Contact problem at C-Fan Motor Connector,
Defective Motor Wire)
③ Check the motor rotating pulse input upon Fan Motor
operation. (Refer to Fan-Motor Circuit in this manual)
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan)
(Twin / Bespoke Mono C,D)

## Slide 174
5. Self Diagnosis & Trouble Shooting
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan)
Start
It reads DC7~12
between MAIN PCB
GND and CN710_3 #10.
YES
FAN operates.
NO
The Compressor is Off.
Run Forced Operation
YES
NO
- This refrigerator uses the BLDC Fan Motor.
The BLDC Motor operates with DC 7~12V.
- The F-Fan motor generally runs together with the compressor.
☞ When checking with the Self Diagnosis
Apply power in 7 minutes after turning the motor off.
(To prevent the compressor from being overloaded)
NO
Upon the initial power on, the compressor and the C-Fan operate. And, this function starts operating when the compressor is about to run right after an instant power outage.
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 175
5. Self Diagnosis & Trouble Shooting
YES
Replace MAIN PCB
NO
Does it read DC7~12V
(between MAIN PCB GND and CN710_3 #10) and lower than DC 2V(between MAIN PCB GND and CN710_3 #11)?
YES
◆Note : C-FAN Operations by Ambient Temperature 1. 29℃ or higher : Turns on after a 10 minute pause when the Compressor starts operating. 2. 18℃~28℃ : Turns on immediately when the Compressor starts operating. 3. 18℃ or higher : Turns off after a minute when the Compressor stops operating. 4. 17℃ or lower : Turns on when the Compressor starts operating. (But, the C-FAN turns on when the C-FAN is detected as bein g ristricted for an hour continually). 5. 17℃ or lower : Turns off (for up to 150 minutes) when the Compressor stops operating.
◆ Possible Causes
① Defective FAN-MOTOR
② Contact problem at the terminal
(MAIN PCB CONNECTOR-TERMINAL (CN710_3. 9,10,
11), Contact problem at C-Fan Motor Connector,
Defective Motor Wire)
③ Check the motor rotating pulse input upon Fan Motor
operation. (Refer to Fan-Motor Circuit in this manual)
5-2-3. When the C-Fan does not operate (Applies to Models with C-Fan)
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 176
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
Start
Defrost Sensor is normal?
(Check it with Self-Diagnosis
YES
Replace the Sensor
NO
☞ When checking with the Self Diagnosis
All Defrost Heaters
are normal?
Check Bimetal, Heater
Continuity or Wire Connection
NO
YES
- When there is a trouble in defrosting, select the Self-Diagnosis function before turning off the unit.
And, check if there is any defect in the Defrost Heater. If not, plug out the unit and do the Trouble-Shooting.
(Refer to the Self-Diagnosis function and check the details)
** Heater Resistance Reading Location ** F-DEF : Resistance between CN72 #3 (WHT) ↔CN72 #1 (BLK) should be 260 ohm ± 10%. ** 0Ω : Short / ∞Ω : Open (Bimetal / Thermal Fuse / Heater Defect)
** Sensor Resistance Reading Location ** F-DEF : Between CN1 #8 (PRP) ↔ CN1 #7 (W/GRY) ** 0Ω : Short / ∞Ω : Open
Temp vs. Resistance Table |  | 
30℃ | 4.22㏀ | For more detail data, refer to DATA1. Temp Table
20℃ | 6.05㏀ | 
10℃ | 8.87㏀ | 
0℃ | 13.29㏀ | 
-10℃ | 20.42㏀ | 
-20℃ | 32.23㏀ | 
-30℃ | 52.41㏀ | 
Refer to Self-Diagnosis
(Twin / Bespoke Mono C,D)

## Slide 177
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
YES
Forced Operation for a while
NO
The Sensor Temperature Value
is lower than 8℃.
YES
Do Forced Defrost
Power is applied to
F-Defrost Heater.
NO
YES
** Sensor Voltage Reading Location ** F-DEF : Between PCB COMMON Ground and CN1 #8 ** 0V : Short / 5V : Open
After pressing the Freezer and the Fridge buttons simultaneously for 4 seconds, push the Freezer button to enter the Test Mode. And then, when any one of the buttons is pressed twice, the Forced Defrost will start and the relevant LED Lamp will light up on the display panel.
(Twin / Bespoke Mono C,D)

## Slide 178
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
After heating up
for a while, it goes back to
Cooling Operation
YES
NO
Normal
Check the related sensors
if they are defective.
Note When the temperature of the F DEF Sensor goes over 8℃ with the Defrost Heater heating up, it stops heating and it goes back to Cooling Operation.
MAIN PCB
Connection is normal?
Repair Connector
NO
YES
Check Bimetal, Heater Wire Cut or Wire Contact
Repair Defective Relay or
replace PCB Assy
YES
(Twin / Bespoke Mono C,D)

## Slide 179
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
Start
Defrost Sensor is normal?
(Check it with Self-Diagnosis
YES
Replace the Sensor
NO
☞ When checking with the Self Diagnosis
All Defrost Heaters
are normal?
Check Bimetal, Heater
Continuity or Wire Connection
NO
YES
- When there is a trouble in defrosting, select the Self-Diagnosis function before turning off the unit.
And, check if there is any defect in the Defrost Heater. If not, plug out the unit and do the Trouble-Shooting.
(Refer to the Self-Diagnosis function and check the details)
** Heater Resistance Reading Location ** F-DEF : Resistance between CN70 #3 (WHT) ↔CN70 #1 (BLK) should be 260 ohm ± 10%. ** 0Ω : Short / ∞Ω : Open (Bimetal / Thermal Fuse / Heater Defect)
** Sensor Resistance Reading Location ** F-DEF : Between CN30 #6 (PRP) ↔ CN30 #7 (W/GRY) ** 0Ω : Short / ∞Ω : Open
Temp vs. Resistance Table |  | 
30℃ | 4.22㏀ | For more detail data, refer to DATA1. Temp Table
20℃ | 6.05㏀ | 
10℃ | 8.87㏀ | 
0℃ | 13.29㏀ | 
-10℃ | 20.42㏀ | 
-20℃ | 32.23㏀ | 
-30℃ | 52.41㏀ | 
Refer to Self-Diagnosis
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 180
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
YES
Forced Operation for a while
NO
The Sensor Temperature Value
is lower than 8℃.
YES
Do Forced Defrost
Power is applied to
F-Defrost Heater.
NO
YES
** Sensor Voltage Reading Location ** F-DEF : Between PCB COMMON Ground and CN30 #6 (or SEN_2) ** 0V : Short / 5V : Open
After pressing the Freezer and the Fridge buttons simultaneously for 4 seconds, push the Freezer button to enter the Test Mode. And then, when any one of the buttons is pressed twice, the Forced Defrost will start and the relevant LED Lamp will light up on the display panel.
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 181
5. Self Diagnosis & Trouble Shooting
5-2-4. When Defrost does not work (F DEF Heater)
After heating up
for a while, it goes back to
Cooling Operation
YES
NO
Normal
Check the related sensors
if they are defective.
Note When the temperature of the F DEF Sensor goes over 8℃ with the Defrost Heater heating up, it stops heating and it goes back to Cooling Operation.
MAIN PCB
Connection is normal?
Repair Connector
NO
YES
Check Bimetal, Heater Wire Cut or Wire Contact
Repair Defective Relay or
replace PCB Assy
YES
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 182
5. Self Diagnosis & Trouble Shooting
5-2-5. When there is No Power
Start
The unit is plugged In?
Plug in the unit
NO
MAIN PCB Fuse is blown?
YES
YES
Check the wire connections
NO
DC310~340V is
applied at BD101 terminals?
YES
NO
220~240V is applied
at MAIN PCB
CN10 #1 and #3?
1) Replace Fuse (AC 250V 6.3A)
2) Replace PCB ASS'Y
- When checking the MAIN PCB, refer to the Operation descriptions and the "Reference" section.
Replace PCB ASS'Y
DC 5V is supplied between PW101
Terminals #14 - #16?
YES
NO
There is AC220~240V or DC310~340V at the MAIN PCB
Power Circuit. So, be cautious
when repairing the unit or
measuring values.
Caution
NO
YES
Replace PCB ASS'Y
(Twin / Bespoke Mono C,D)

## Slide 183
5. Self Diagnosis & Trouble Shooting
5-2-5. When there is No Power
5V is applied at
CE105 terminals?
YES
YES
YES
NO
Panel PCB operates normally?
YES
DC 12V is applied at
CE113 terminals?
Loads such as Relay
operate normally?
Normal (Check again)
Replace PCB ASS'Y
NO
- Check the connection of Door Panel PCB
NO
1) Check the wire connections
2) Replace Panel PCB
1) Check Lead Wire connections
2) Replace Relay or PCB ASS'Y
NO
NO
Replace PCB ASS'Y
YES
Is there PCB Short
or breakage?
YES
1) Do Re-soldering
2) Replace PCB MAIN
(Twin / Bespoke Mono C,D)

## Slide 184
5. Self Diagnosis & Trouble Shooting
5-2-5. When there is No Power
Start
The unit is plugged In?
Plug in the unit
NO
MAIN PCB Fuse is blown?
YES
YES
Check the wire connections
NO
DC310~340V is
applied at BD101 terminals?
YES
NO
220~240V is applied
at MAIN PCB
CN10 #1 and #3?
1) Replace Fuse (AC 250V 6.3A)
2) Replace PCB ASS'Y
- When checking the MAIN PCB, refer to the Operation descriptions and the "Reference" section.
Replace PCB ASS'Y
DC 6.2V is supplied between PW101
Terminals #3 - #12?
YES
NO
There is AC220~240V or DC310~340V at the MAIN PCB
Power Circuit. So, be cautious
when repairing the unit or
measuring values.
Caution
NO
YES
Replace PCB ASS'Y
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 185
5. Self Diagnosis & Trouble Shooting
5-2-5. When there is No Power
5V is applied at
CE105 terminals?
YES
YES
YES
NO
Panel PCB operates normally?
YES
DC 12V is applied at
CE113 terminals?
Loads such as Relay
operate normally?
Normal (Check again)
Replace PCB ASS'Y
NO
- Check the connection of Door Panel PCB
NO
1) Check the wire connections
2) Replace Panel PCB
1) Check Lead Wire connections
2) Replace Relay or PCB ASS'Y
NO
NO
Replace PCB ASS'Y
YES
Is there PCB Short
or breakage?
YES
1) Do Re-soldering
2) Replace PCB MAIN
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 186
5. Self Diagnosis & Trouble Shooting
5-2-6. When the Compressor is not working
Start
10 minutes have passed since COMP was off
Check in 10 Min
When Forced Operation mode is activated, COMP operates
Temperature Sensor is normal?
Is DC 15V applied to TD501?
Temperature sensing part of MAIN PBA is Good
Replace MAIN PBA or Repair the connection
YES
NO
NO
NO
NO
YES
YES
YES
YES
Refer to the TEST Function in this manual
Replace the Sensor
Repair the sensing
part or Replace MAIN PBA
NO
Replace MAIN PBA
Forced Operation signal sound should be checked
YES
When the inverter LED is ON, it indicates that the compressor does operate normally
(Twin / Bespoke Mono C,D)

## Slide 187
5. Self Diagnosis & Trouble Shooting
CN10_1/CN102 Connector is Good
YES
NO
Check the COMP wire
Check the Compressor
Check AC Power wire
YES
NORMAL(Recheck)
☞ SMPS Primary Voltage checking : REG101, REG102 Terminal(Input and GND) : DC15V±1.5V Terminal(Output and GND) : DC5V±0.25V
COMP ASS'Y is Good
YES
NO
Replace COMP ASS'Y
5-2-6. When the Compressor is not working
(Twin / Bespoke Mono C,D)

## Slide 188
5. Self Diagnosis & Trouble Shooting
5-2-6. When the Compressor is not working
Start
10 minutes have passed since COMP was off
Check in 10 Min
When Forced Operation mode is activated, COMP operates
Temperature Sensor is normal?
Is DC 15V applied to ZD501?
Temperature sensing part of MAIN PBA is Good
Replace MAIN PBA or Repair the connection
YES
NO
NO
NO
NO
YES
YES
YES
YES
Refer to the TEST Function in this manual
Replace the Sensor
Repair the sensing
part or Replace MAIN PBA
NO
Replace MAIN PBA
Forced Operation signal sound should be checked
YES
When the inverter LED is ON, it indicates that the compressor does operate normally
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 189
5. Self Diagnosis & Trouble Shooting
CN11/CN102 Connector is Good
YES
NO
Check the COMP wire
Check the Compressor
Check AC Power wire
YES
NORMAL(Recheck)
☞ SMPS Primary Voltage checking : REG103 Terminal(Input and GND) : DC15V±1.5V Terminal(Output and GND) : DC5V±0.25V
COMP ASS'Y is Good
YES
NO
Replace COMP ASS'Y
5-2-6. When the Compressor is not working
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 190
5. Self Diagnosis & Trouble Shooting
Start
Door stays open?
Water penetrates into
Door S/W?
MICOM #1 and #5
Voltage changes when the Door is open/close?
Closed
YES
YES
Check if there is any obstacle
pushing the Door open.
Replace Door S/W
NO
Repair Wire Cut / Door S/W
Door & MICOM State | 
Door | R MICOM(#1) F DOOR : MICOM(#5)
Close | 0V(Low)
Open | 5V(High)
NO
① When there is "Ding Dong" sound not stopping
Gap exists
5-2-7. When the unit keeps alarming (Buzzer Sound)
Reference
Fridge / Freezer Door Open Alarm : It sends out an alarm sound when it passes over 2 minutes after the door is open. And, when the door remains open, it will keeps alarming every minute.
When the door is not closed properly, MICOM recognizes it as Door Open and sends out an alarm sound. When it passes over 10 minutes after it recognizes the Door Open, the room lamps will be off. At this time, when the Door is completely open, the Lamp will not be on right away, but after a while.
This document cannot be used without Samsung's authorization

## Slide 191
5. Self Diagnosis & Trouble Shooting
5-2-7. When the unit keeps alarming (Buzzer Sound)
Door S/W is in good
condition?
YES
YES
NO
Replace Door S/W
Check MAIN PCB and Door S/W
※Note F-DOOR S/W only applies to models for STIWA.
YES
Connector (CN30 or CN1) is
inserted properly?
NO
Insert the Connector
This document cannot be used without Samsung's authorization

## Slide 192
5. Self Diagnosis & Trouble Shooting
5-2-7. When the unit keeps alarming (Buzzer Sound)
Start
The unit is not in
Forced Operation or Forced
Defrost mode.
When the unit is
plugged out and in again, it
keeps beeping?
YES
NO
MAIN PCB is normal
Check if there is any foreign
substance at Test Jumper of MAIN PCB or any part shorted out
Cancel Forced Operation/Defrost
NO
YES
② When it keeps 'Beeping'
This document cannot be used without Samsung's authorization

## Slide 193
5. Self Diagnosis & Trouble Shooting
5-2-7. When the unit keeps alarming (Buzzer Sound)
This model has a buzzer affixed on the MAIN PCB. If there is no buzzer sound upon button press, Forced Operation or Door Open, disconnect MAIN PCB and check if the buzzer is damaged or there is any defective soldering. (If it is not a soldering problem, it is recommended replacing MAIN PCB due to difficulties in repairing)
※ It may not be able to check when it is a closed built-in environment and there is lots of noise around.
③ No Buzzer Sound
YES
YES
Door Alarm goes off when
any one of Fridge & Freezer doors remains being open over 2 minutes.
Normal
NO
"DingDong" sound
goes off when a button on the display panel is pressed.
YES
Start
BUZZER Breakage ----
Replacement
Any breakage or kink
in MAIN PCB BUZZER
Check & Replace MAIN PCB BUZZER
NO
YES
This document cannot be used without Samsung's authorization

## Slide 194
5. Self Diagnosis & Trouble Shooting
5-2-7. When the unit keeps alarming (Buzzer Sound)
Solder lead comes off the
BUZZER vibration plate.
NO
YES
NO
Check the button pressing force and structural design (Door Sensing)
Replace MAIN PCB
This document cannot be used without Samsung's authorization

## Slide 195
5. Self Diagnosis & Trouble Shooting
5-2-8. When PANEL PCB operates abnormally
Start
The connector on
the Display Panel is inserted
properly.
MAIN PCB Connector
(CN50 or CN51) is inserted properly
YES
YES
DOOR PANEL PCB
Connector is inserted properly
NO
YES
It lights up when
PANEL-PCB is being
replaced
NO
NO
NO
Defective PANEL PCB
YES
When PANEL KEY is not selected
① Check Fridge Door Wiring - Short or Open Wire
② Check CABI Upper Wiring - Short or Open Wire
③ Check Short/Open at MAIN PCB Panel Lamp Circuit
Re-insert Connector,
Correct the defective contact
Re-insert MAIN PCB Connector
Re-insert Connector,
Correct the defective contact
① When PANEL PCB does not light up or partially does
- Display Assy Location 1. Internal Type : Top Table 2. External Type : Fridge Door/Top Hinge
This document cannot be used without Samsung's authorization

## Slide 196
5. Self Diagnosis & Trouble Shooting
5-2-8. When PANEL PCB operates abnormally
There are no buttons
being pressed continuously.
The trouble continues
with PCB being removed
When PANEL-PCB
is being replaced, it works
normal.
② When Panel PCB buttons are not working
YES
YES
When being separated, it works
Being Pressed
※ When the trouble is being remained after the above,
NO
Defective PANEL PCB
YES
① Check Fridge Door Wire - Short or Open Wire
② Check CABI Upper Wiring - Short or Open Wire
③ Check Short/Open at MAIN PCB Panel Communication/Power- Supply Circuit
Re-assemble PCB ASS'Y,
Correct any restrictions on the buttons
Re-assemble PCB ASS'Y,
Correct any restrictions on the buttons
This document cannot be used without Samsung's authorization

## Slide 197
5. Self Diagnosis & Trouble Shooting
5-2-9. When the Room Lamp (LED) does not light up
Start
DOOR S/W works
normal (Open/Close)
NO
YES
Door & MICOM State | 
Door | MICOM(#1)
 | Top
Close | 0V(Low)
Open | 5V(High)
MIC01 MICOM #1 Output
Voltage is normal
NO
YES
Check & Replace DOOR S/W
Voltage Output at Pin
#1 (CN1) is
normal
NO
YES
Voltage Output at the
MAIN PCB Connector
(CN1 #28) is normal (10~12V)
NO
YES
Check Connector Terminal /
Replace PCB
The LED Lamp is
connected properly
NO
Check Connector Terminal
MICOM State | 
Micom | #1
Close | 0V(Low)
Open | 5V(High)
Replace / Repair PCB
Replace PCB
Connector Terminal | 
Connector | CN1 1 Pin
0V(Low) | 0V(Low)
5V(High) | 10~12V(High)
YES
(Twin / Bespoke Mono C,D)

## Slide 198
5. Self Diagnosis & Trouble Shooting
5-2-9. When the Room Lamp (LED) does not light up
The LED Lamp is ok
Replace LED LAMP
Normal
NO
YES
YES
(Twin / Bespoke Mono C,D)

## Slide 199
5. Self Diagnosis & Trouble Shooting
5-2-9. When the Room Lamp (LED) does not light up
Start
DOOR S/W works
normal (Open/Close)
NO
YES
Door & MICOM State | 
Door | MICOM(#46)
 | Right
Close | 0V(Low)
Open | 5V(High)
MIC01 MICOM #46 Output
Voltage is normal
NO
YES
Check & Replace DOOR S/W
Voltage Output at Pin
#20 (CN30) is
normal
NO
YES
Voltage Output at the
MAIN PCB Connector
(CN30 #28) is normal (10~12V)
NO
YES
Check Connector Terminal /
Replace PCB
The LED Lamp is
connected properly
NO
Check Connector Terminal
MICOM State | 
Door (Right and Left) | R
 | #46
Close | 0V(Low)
Open | 5V(High)
Replace / Repair PCB
Replace PCB
IC74(R) | 
Micom | CN30 20 Pin
0V(Low) | 0V(Low)
5V(High) | 10~12V(High)
YES
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 200
5. Self Diagnosis & Trouble Shooting
5-2-9. When the Room Lamp (LED) does not light up
The LED Lamp is ok
Replace LED LAMP
Normal
NO
YES
YES
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 201
5. Self Diagnosis & Trouble Shooting
5-2-10. When Fridge Damper does not work
Start
DAMPER is under a
working condition.
NO
YES
Damper operates with
DOOR S/W closed.
NO
NO
Forced Operation, Temp Increased
DOOR S/W is good
NO
YES
Fridge temp satisfies
the set temp
NO
YES
Check Wiring & PCB MAIN
DAMPER is good
Replace DOOR S/W
Door & MICOM State | 
Door | MICOM (#1)
Close | 0V
Open | 5V
Shift Set Temp [Set lower than the current temp]
(Twin / Bespoke Mono C,D)

## Slide 202
5. Self Diagnosis & Trouble Shooting
5-2-10. When Fridge Damper does not work
MAIN PCB Connector
CN90_2 is inserted normal
NO
YES
NO
Check Connector CN90_2
DAMPER is normal
YES
Replace DAMPER
Normal
Replace PCB MAIN
(Twin / Bespoke Mono C,D)

## Slide 203
5. Self Diagnosis & Trouble Shooting
5-2-10. When Fridge Damper does not work
Start
DAMPER is under a
working condition.
NO
YES
Damper operates with
DOOR S/W closed.
NO
NO
Forced Operation, Temp Increased
DOOR S/W is good
NO
YES
Fridge temp satisfies
the set temp
NO
YES
Check Wiring & PCB MAIN
DAMPER is good
Replace DOOR S/W
Door & MICOM State | 
Door | MICOM (#46)
Close | 0V
Open | 5V
Shift Set Temp [Set lower than the current temp]
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 204
5. Self Diagnosis & Trouble Shooting
5-2-10. When Fridge Damper does not work
MAIN PCB Connector
CN90_3 is inserted normal
NO
YES
NO
Check Connector CN90_3
DAMPER is normal
YES
Replace DAMPER
Normal
Replace PCB MAIN
This document cannot be used without Samsung's authorization
(Mono C,D,E,F / Bespoke Mono E,F)

## Slide 205
5. Self Diagnosis & Trouble Shooting
Is the Wi-Fi module embedded connected?
Is Wi-Fi enabled?
Wi-Fi Easy Setup has been implemented.
Assemble the module
Enable Wi-Fi
Perform Easy Setup.
Monitor mode begins properly?
In case an error is detected:
1 | TX
2 | RX
3 | RST
4 | GND
5 | VCC
Is the Easy Setup complete?
“Samsung Fridge_E50AJTRBXX" appears from the AP List in SET AP mode.
Port | Standby
TX | 0-5V swing
RX | 0-5V swing
RST | 5V
VCC | 5V or 12V
Normal
Replace the defective module.
No
Yes
Yes
Yes
Yes
Yes
Yes
No
No
No
No
No
Check the router power
Yes
This document cannot be used without Samsung's authorization
Factory Reset
(one time)
Still not appears AP list
Factory Reset Guide:
1) Hold a “O“ button until display ‘AP’ in display panel (about 5sec)
2) When “AP” display, Hold again “O“ button until display ‘rS’ in display panel (about 10sec)
5-2-11. When the Wi-Fi does not work properly
☞ When checking with the Self Diagnosis

## Slide 206
5. Self Diagnosis & Trouble Shooting
If Failure Condition is detected during compressor is operating, immediately stop Compressor operating and stand by 5 minutes. During this 5 minutes, RPM command signal is not available. It means, even if available RPM command signal is applied to the compressor, it does not work and keep standing by.
Blinking time is 1 second and dwell time is 2 seconds.
LED blinking frequency depending on protecting functions
LED blinking frequency depending on protecting functions If the same blinking, After 5 minutes, Follow the Remarks
Protecting Functions | LED Displaced diagram | Remarks
Normal Operation |  | N/A
Starting Failure |  | 1. Short between COMP U,V, and W phase (CN102) 2. Short among IPM Pins (No. #1~24) 3. Drop the IPM operating Voltage under DC 13.5V 4. Other cases, check the COMP, cycle, etc.
IPM Fault |  | 
Abnormal Current Detection |  | 1. Open the COMP wire (CN102) 2. Bad condition of resistor R1(ex. Bad soldering) 3. Other cases, check the COMP, cycle, etc.
Motor Locked / Over RPM |  | 1. Check PBA Bottom side soldering state. 2. Check Input voltage oscillation 3. Other cases, check the COMP, cycle, etc.\
Low Voltage |  | Check Input voltage under AC 53V(Input power AC 110~127V) or AC 106V(Input power AC 220~240V)
Over Voltage |  | Check Input voltage under AC 155V(Input power AC 110~127V) or AC 310V(Input power AC 220~240V)
Communication error |  | 1. Main-Inverter communication error
IPM Shut-down |  | 1. IPM temperature rise above 120°C

## Slide 207
6-1. PART Layout (Twin / Bespoke Mono C,D)
1. Inverter COMP control
2. SMPS : Supply the stable DC voltage
3. Noise filter : Protection from internal
/ external noise, removes EMI noise
4. Main & EEPROM : Load control and data storage
5. Relay Block : AC load control(Heater control)
6. Sensor, Switch, Room Fan Motor control
7. Main ↔ Display signal transmission
Main ↔ Wifi Module commnication
8. Room Lamp control
9. Step Valve and COMP Fan motor control
10. Damper & Ice Maker Control
This document can not be used without Samsung's authorization
6. PCB Diagram

## Slide 208
6-1. PART Layout (Mono C,D,E,F / Bespoke Mono E,F)
1. Inverter COMP control
2. SMPS : Supply the stable DC voltage
3. Noise filter : Protection from internal
/ external noise, removes EMI noise
4. Main & EEPROM : Load control and data storage
5. Relay Block : AC load control(Heater control)
6. Sensor, Switch(Include Rotary Switch)
, Fan Motor control
7. Main ↔ Display signal transmission
8. Room Lamp control
This document can not be used without Samsung's authorization
6. PCB Diagram

## Slide 209
6-2. Connector Layout & Description (Twin / Bespoke Mono C,D)
This document can not be used without Samsung's authorization
6. PCB Diagram
CN50. UART Display
12 : GND
14 : TX
16 : RX
22 : VCC
CN1 SENSOR/ SWTICH/ FAN
1 : R DOOR S/W
5 : Humidity SENSOR
9 : EXT SENSOR
13 : F ROOM SENSOR
19 : F-FAN
21 : F-FAN F/G
2 : VCC
4 : F DOOR S/W
8 : F DEF SENSOR
12 : R ROOM SENSOR
18 : R-LAMP
28 : R-DEF SENSOR
3,7,11,15,17,23,6,10,14,16,22: GND
CN10 AC INPUT
1 : N1
2 : N2
CN72 AC Input/Load
1 : N2
3 : F-DEF HEATER
5 : N/A
7 : F/G
CN102 COMP
1 : COMPSIGNAL_U
3 : COMPSIGNAL_V
5 : COMPSIGNAL_W
CN70 C-FAN
1 : Step Valve A
2 : Step Valve B
3 : Step Valve VCC
4 : Step Valve /A
5 : Step Valve /B
6 : C-FAN GND
7 : C- FAN
8 : C- FAN FG
CN90_2 DAMPER
1 : AOUT1
2 : AOUT2
3 : BOUT2
4 : BOUT1
CN03 WIFI&HASS
1 : VCC
2 : RX
3 : TX
4 : GND
5 : RESET

## Slide 210
6-2. Connector Layout & Description (Mono C,D,E,F / Bespoke Mono E,F)
This document can not be used without Samsung's authorization
6. PCB Diagram
CN51. UART Display
8 : GND
10 : TX
12 : RX
14 : VCC
CN10 AC INPUT
1: N1
2: N2
CN70 AC Input/Load
1 : N/A
3 : N/A
5 : N/A
7 : F/G
CN102 COMP
1 : COMPSIGNAL_U
3 : COMPSIGNAL_V
5 : COMPSIGNAL_W
CN710_3 C-FAN
1 : GND
2 : INPUT
3 : FG
CN90_3 DAMPER
1 : AOUT1
2 : AOUT2
3 : BOUT2
4 : BOUT1
CN30 SENSOR/ SWTICH/ FAN
1 : R DOOR S/W
5 : EXT SENSOR
6 : F DEF SENSOR
9 : KNOB(ROTARY S/W)
10 : F DOOR S/W
13 : F ROOM SENSOR
19 : F-FAN
21 : F-FAN F/G
14 : R ROOM SENSOR
20 : R ROOM LAMP
27 : DC 5V
23,24,25,26 : STEP VALVE
28 : DC 12V
3,7,11,15,17,4,8,12,16,18 : GND

## Slide 211
6-3. Connector Layout & Description (Wi-Fi Module)
6. PCB Diagram
1 | VCC
2 | RX
3 | TX
4 | RST
5 | GND
ANT1
Shield CAN
CONNECTOR
1
5

## Slide 212
7. Wiring Diagram
7-1. Wiring Diagram (Twin / Bespoke Mono C,D)

## Slide 213
7. Wiring Diagram
7-2. Wiring Diagram (Bespoke Mono E,F/ Mono C,D,E,F)

## Slide 214
8. Block Diagram
8-1. PBA Main (Twin / Bespoke Mono C,D)
This document can not be used without Samsung's authorization

## Slide 215
MICOM
RESET Circuit
Oscillator
Load Control
Circuit
EEPROM
DIODE Option
LOAD SECTION
PBA MAIN
EMI
FILTER
AC POWER
INPUT
F Room
F DEF
Ambient
SENSOR
Sensor Sensing
Circuit
DOOR S/W
LED Control
KEY Control
Display Panel
PCB
Display Control
Circuit(LED)
AC Power
DC Power
Signal
DC 12V, 5V
DC 12V
DC 5V
Motor Operating Part
FG Developing Part
F Room
BLDC FAN
BLDC Motor
Control Circuit
DC 5V
DC 12V
220V~240V /50Hz,60Hz
COMP.
R Room Lamp
LED PCB
DC 12V
LED Drive
Circuit
Door S/W
Sensing Circuit
Inverter PBA
INV
Comp.
SMPS Circuit
Inverter
Control Circuit
F DEF Heater
Power Stage
Signal Stage
R Door
R Room
R Room
DAMPER
DC 12V
Damper
Control Circuit
SMPS Circuit
F Door
KNOB
8. Block Diagram
8-1. PBA Main (Mono C,D,E,F / Bespoke Mono E,F)
This document can not be used without Samsung's authorization
Buzzer Control

## Slide 216
9-1. Nomenclature
9. Reference Information
 |  |  | Capacity |  |  |  | Year |  | Grade |  | Feature 1 |  |  |  |  | Feature 2 |  |  |  |  |  |  |  |  | Feature 3 |  |  |  | Color |  |  | 
 |  |  |  |  |  |  |  |  |  |  | (Exterior) |  |  |  |  | (Interior) |  |  |  |  |  |  |  |  | (Energy) |  |  |  |  |  |  | 
Code | R | B |  | 3 |  | 4 | K |  | 6 |  | 0 |  |  |  |  | 0 |  |  |  |  |  |  |  |  | 0 |  |  |  | 7F |  |  | 
Feature | BMF |  | Capacity | Capacity |  |  |  | Options | Series |  | No | Control Ex/In | Water Dispenser | Handle | Wifi | No | Upper Box | Lower Box | 2 Step Foldable shelf | Bottle Rack | Shelf Trim Deco | Box | Series | Height | No | Energy New | Energy Old | Cooling | Color | Bespoke | Handle Deco (Recess Only) | Color Name
RB7300T | R | B | 185cm | 3 | 4 |  | T | Energy C~F, Bending | 6 | Blue resin | 0 | Internal | - | Recess | - | 0 | - | Nomal Veg | - | - | - | 1Box | 6 series | ALL | F | F | A+ | Mono | SR | No | Yes | REAL STAINLESS
 |  | (L) | 193cm | 3 | 6 |  | A | Energy A~3, Bending / Energy A~F, BESPOKE |  |  | - |  |  |  |  | 1 | - | Nomal Veg | Yes | - | - | 1Box | 6 series | ALL | E | E | A++ | Mono | B1 | No | Yes | BLACK DOI
 |  |  | 203cm | 3 | 8 |  |  |  | 7 | Metal Cooling & Gray resin | 2 | Internal | - | Bar | - | 2 | - | Nomal Veg | - | Yes | - | 1Box | 6 series | ALL | D | D | A++ | Mono | S9 | No | Yes | REFINED INOX(MATT DOI METAL)
 |  |  |  |  |  |  |  |  |  |  | 3 | Internal | Yes | Recess | - | 3 | Fresh+ | humidity control | - | - | - | 2Box | 6 series | ALL | C | C | A+++ -10% | Mono | EL | No | - | Shell Beige
 |  |  |  |  |  |  |  |  |  |  | - |  |  |  |  | 4 | Fresh+ | humidity control | Yes | - | Yes | 2Box | 6, 7 series | ALL | 3 | C | A+++ -10% | TWC | BN | No | - | NEW EMPIRE BLACK
 |  |  |  |  |  |  |  |  |  |  | 5 | External | Yes | Recess | - | 5 | Fresh+ | humidity Control | - | Yes | Yes | 2Box | 6, 7 series | ALL | B | B | A+++ -40% | TWC | SA | No | - | Metal Graphite
 |  |  |  |  |  |  |  |  |  |  | 6 | External | - | Bar | - | 6 | Fresh+ | humidity control | Yes | Yes | Yes | 2Box | 6, 7 series | RB38 ONLY | A | A | A+++ -50% | TWC | WW | No | - | Snow White
 |  |  |  |  |  |  |  |  |  |  | 7 | External | - | Recess | - | 7 | Fresh | Nomal Veg | - | - | - | 2Box | 6, 7 series | ALL | T | A | A -10% | TWC | 12 | Yes | - | CLEAN WHITE
 |  |  |  |  |  |  |  |  |  |  | 8 | External | - | Recess | Yes | 8 | Fresh | Nomal Veg | Yes | - | - | 2Box | 6, 7 series | ALL | 2 | A++ CIS | A++ CIS | Mono | 17 | Yes | - | GLAM PEACH
 |  |  |  |  |  |  |  |  |  |  | 9 | External | Yes | Recess | Yes | 9 | Fresh | Nomal Veg | - | Yes | - | 2Box | 6, 7 series | ALL | 1 | 국판 1등급 | 국판 1등급 | Mono | 18 | Yes | - | CLEAN VANILLA
 |  |  |  |  |  |  |  |  |  |  | B | Internal | - | BESPOKE Recess | - | G | Nomal | humidity control | Yes | Yes | Yes | 2Box | 6, 7 series | RB38 ONLY |  |  |  |  | 22 | Yes | - | CLEAN BLACK
 |  |  |  |  |  |  |  |  |  |  | C | Internal | - | BESPOKE Recess | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  | 27 | Yes | - | SATIN GRAPHITE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 34 | Yes | - | SATIN NAVY
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 35 | Yes | - | GLAM WHITE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 38 | Yes | - | GLAM LAVENDER
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 39 | Yes | - | SATIN BEIGE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 41 | Yes | - | CLEAN NAVY
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 48 | Yes | - | SATIN SKY BLUE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 3K | Yes | - | CLEAN PEACH
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | AP | Yes | - | PANEL READY
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CE | Yes | - | COTTA PCM BEIGE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CL | Yes | - | COTTA PCM LAVENDER
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CS | Yes | - | COTTA PCM SKY BLUE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CW | Yes | - | COTTA PCM WHITE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | VG | Yes | - | METAL GRAPHITE
Feature 1
(Exterior)
Feature 2
(Interior)

## Slide 217
9-1. Nomenclature (Mass zone)
9. Reference Information
RB33B612ESA/EF
Capacity
Series
Ext
Int
Energy
CMF

## Slide 218
9-2. Trouble Shooting
9. Reference Information
Problem | What To Do
The appliance is not operating at all or the temperature is too high. | • Check that the power plug is correctly connected. • Is the temperature control on the front panel correctly set? • Does sun shine on the appliance or are there heat sources nearby? • Is the back of the appliance too near to the wall?
The food in the refrigerator is frozen. | • Is the temperature control on the front panel set to the coldest temperature? • Is the surrounding temperature too low? • Did you store the food with a high water content in the coldest part of the fridge?
There are unusual noises. | • Check that the appliance is installed on a stable, level floor. • Is the back of the appliance too near to the wall? • Have any foreign objects fallen behind or under the appliance? • Is the noise coming from the compressor in the appliance? • A ticking sound may be heard inside the appliance; this is normal. This sound occurs when the various accessories contract or expand.

## Slide 219
Problem | What To Do
The front corners and sides of the appliance are warm and condensation starts to form. | • Heat-proof pipes are installed in the front corners of the appliance to prevent condensation from forming. When the surrounding temperature rises, this may not always be effective. However, this is not abnormal. • In very humid weather, condensation may form on the outer surface of the appliance when the moisture in the air comes into contact with the cool surface of the appliance.
You can hear a liquid bubbling in the appliance. | • This is the refrigerant, which cools the inside of the appliance.
There is a bad smell inside the appliance. | • Has a food item spoiled? • Make sure that strong smelling food (for example, fish) is wrapped so that it is airtight. • Clean out your freezer periodically and throw away any spoiled or suspect food.
9-2. Trouble Shooting
9. Reference Information

## Slide 220
Problem | What To Do
There is a layer of frost on the appliance walls. | • Are the air outlet vents blocked by food stored inside the refrigerator. • Space the food out as much as possible to improve ventilation. • Is the door fully closed?
Condensation forms on the inside wall of the appliance and around vegetables. | • Food with a high water content is stored uncovered with a high humidity level or the door has been left open for a long time. • Store the food with a cover or in sealed containers.
9-2. Trouble Shooting
9. Reference Information

## Slide 221
9-3. Q&A
Descriptions of symptoms | Check Points | Corrective Measures
▶ Noise (resonance) problems keep on even though the noise generating BLDC motors for both of the compartments are replaced several times. What does generate the resonance and how can it be settled down? | When the BLDC fan motor rotates in low RPM, The friction with air is quite high and it generates “grinding” noises. | If you replace the ambient thermistor with a 2.7K resistance (detecting 43℃), the BLDC fan motor rotates in high RPM, which reduces friction with air resulting in reduction of the “grinding” resonance.
▶ What causes the “knocking” noises? How to solve it? | It makes “knocking” or “branch breaking” noises when the liner and the shelves hit each other due to the fluctuation of the inside air pressure upon door open/close. Also, these noises occur when the liners and the shelves hit each other as the liners expand and contract due to the temperature change in both of the compartments. | Check the clearance between the selves and the liners. ① Freezer Shelves: Remove the trim shelves already attached and replace them with those supplied for service. ② Fridge Shelves: Because noise- preventing trim selves are not attached, it needs attaching.
▶ What is the solution if the same problem occurs even though the counter action in the service bulletin has been implemented already for the “knocking” noises? | Check if the selves wobble. If they do, have shelves sit firmly on their places. | 
9. Reference Information

## Slide 222
Descriptions of symptoms | Check Points | Corrective Measures
▶What causes the liquid passing noises from the back of the refrigerator? | Refrigerant goes into the evaporator via the capillary tube in which the refrigerant expands as it circulates the cooling cycle. At this time, the refrigerant is in its liquid state and it starts evaporating as it reaches at the inlet of the evaporator with a bigger diameter, which causes the refrigerant noises. And, it gets worse when the refrigerant does not flow freely. | 
▶What is the solution for the compressor noises? | For new refrigerators | 
 | Check if the refrigerator is leveled. | Check if the refrigerator wobbles by shaking with hands.
 | Check if there is enough clearance at the back of the refrigerator for the ventilation of the machine compartment. | If there is not enough clearance or it is blocked by things such as newspaper, there could be resonance noises.
 | Required clearance around the product. | More than 5cm from the back, 30cm from the top and 10cm from its sides.
9-3. Q&A
9. Reference Information

## Slide 223
Descriptions of symptoms | Check Points | Corrective Measures | 
▶ What is the solution for the compressor noises? | For old refrigerators |  | 
 | Dust could get built-up in the machine compartment. Then, its ventilation would get restricted which makes the refrigerator overheated resulting in the increase of the noise level. |  | Explain it to customers and let them clean dust or any other foreign substances in the machine compartment.
 | As the vibration proof rubbers get hardened, noises generate during the comp operation. (The noise level is quite high.) → Replace the vibration proof rubbers. |  | The compressor is dislocated due to impact during its transportation such as moving-in. →Check if it’s dislocated when it is more noisy after moving-in.
▶ During the comp start-up, iron friction noises occur. What causes them? | The reciprocation piston could get worn out or inner components could get dislocated. |  | 
▶ What can be checked when the unit sends out noises? | 1. Check its symptoms and patterns. 2. Check if the unit is installed on a firm and leveled floor. 3. Check if the unit is installed close to the customer’s living area. 4. Check if the panel on the machine compartment hits on the rear wall and the unit has enough clearance with the rear wall. 5. Check if the refrigerant pipes are shaped as normal. |  | 
9-3. Q&A
9. Reference Information

## Slide 224
Descriptions of symptoms | Check Points | Corrective Measures
▶ Why is the fridge compartment not cool? (Not a defect) | Advise customers to adjust its temperature level to one or two step higher. For example, when the ambient temperature is low such as in winter (especially, when you use it in the morning with the door not being opened or closed during the night), the compartment temperature could get increased by 1~2℃. So, advise customers to shift its temperature level and explain to them that it does not affect its power consumption that much when its temperature setting is adjusted to one or two step lower. | 
▶ Why is the food melt even though the display of the freezer compartment shows -20℃? | Check the compartment temperature with a thermometer. | If it is considered to be low cooling, When the BLDC motor fan does not rotate because its restriction is not picked up. When the evaporator is frozen-up (defrost it) Temp detection error according to the characteristic change of the thermistor (set the compartment temperature or replace the thermistor)
9-3. Q&A
9. Reference Information

## Slide 225
Descriptions of symptoms | Check Points | Corrective Measures
▶ What is the reason that vegetables get frozen even though the fridge compartment is set to MIN? | Replace the fridge thermistor because it could be faulty. 1st: Check if the thermistor works after referring to the self-diagnosis checklist on the MAIN-PCB cover. If the over-cooling keeps on even though there is no problem with the above, replace it. | 
▶ What can be done when frozen food gets melt in the freezer compartment or it does not cool down? | Defrost it by using hot water and check the defrost system for any fault. And then, eliminate the root causes so as to prevent it from reoccurring. | 
▶ Why doesn’t the compressor operate upon power supply? | Upon the initial power on, the compressor starts operating after a five minute delay to protect the compressor. So, please wait until it starts operating. | 
9-3. Q&A
9. Reference Information

## Slide 226
Descriptions of symptoms | Check Points | Corrective Measures
▶ Why does it send out “Ding Dong” or alarm sounds with the doors closed? | Check if the food sticks out preventing the doors from closing properly. If it send out the above sounds with the door closed well, the door switch may not have been pressed down completely. So, make sure for the door switches to be pressed completely. Still, if it does not stop going off, check the wiring connections because the door switch signals may not be inputted into the PCB. And, when the door switch is faulty or it is not pressed down completely, the fan does not rotate and it causes low-cooling advancing to a defrost problem. | 
 | Note : When it comes to automatic models, the fan motor does not operate right on with the door closed after being opened. The fan motor for dual-evaporator refrigerators starts after a 10- second delay and when the ambient temperature is higher than 33℃, it starts after a minute. | 
▶ What can be done when it sends out much smell in the fridge and the freezer compartments after 2 months? ▶ The ice smells odd. | When the stored food sends out much smell. ☞ Check if there is any food sending out sustaining smells. Dried squid, dried laver : Hold on them Pounded garlic : Put it in an airtight container Medical herbs : Make sure they are packed airtight. Replace the old packing or wrap with a new one. Others : Check if the container is sealed or the food is packed airtight. ☞ Check if the compartment temperature is normal and the food is contaminated. ☞ Check if there are any overflow of side dishes on the shelves or the bottom of the compartments. ☞ Put the food sending out much smell in an airtight bag or container. ☞ Open the door and ventilate it. Also, clean liners, shelves, containers and door bins. ☞ If you make ice with tap water, a chlorine odor may occur. It is recommended using mineral water or water filtrated by a water filtration device. | 
9-3. Q&A
9. Reference Information

## Slide 227
Descriptions of symptoms | Check Points | Corrective Measures
▶ What can be done when the Ice Maker dose not produce ice? | ☞ if the freezer temperature is too warm, try setting the freezer temperature lower. ☞ Check if the water tank is filled with water. ☞ Check if you fit the water tank correctly. | 
▶ What can be done when the Water dispenser does not function? | ☞ If the water tank is frozen because the fridge temperature is too low, try selecting a warmer setting on the Digital display. ☞ Check if the water tank is filled with water. ☞ Check if you fit the water tank correctly. | 
 | Note : 1) When it passes 120 seconds after turning on the Water Lever, the Water Solenoid Valve will be turned off stopping the water supply regardless of the state of the Water Lever. 2) After this, it does not supply water for one minute even if the Water Lever is being pushed (on). 3) And then, after the one-minute delay time, water supplies again when the Water Lever is being pushed. | 
9-3. Q&A
9. Reference Information

## Slide 228
Descriptions of symptoms | Check Points | Corrective Measures
▶ What is the cause and its counter action for chemical smells with new products? | During its delivery to customers, chemical smells from various components could build up inside of the compartments. So, please let the doors open for some time to use the unit. | 
 | Precautions : Smells tend to get soaked into the liners or other components. If food generating much smell is stored inside, it would stick onto the liners and other components and it is so difficult to remove the smell. Especially, customers should take care in storing smelly food properly with its sealing being tight during the early period of the product’s use. | 
▶ What can be done when the smell keeps on even thought the deodorizers are cleaned? | 1) Turn off the refrigerator (unplug the unit) and remain the door opened. 2) Take out the food stored in the refrigerator. And then, take out all the shelves, door bins and containers, and put them in warm water. After cleaning them by using dish detergents and drying them, put them back to their locations. 3) Remove the deodorizer and soak it in warm water more than 4 hours. After drying it in sunlight, put it back to its location. 4) Throw away the smell-soaked plastic bags and put the food in new ones. | 
9-3. Q&A
9. Reference Information

## Slide 229
Thank you
- This Service Manual is a property of Samsung Electronics Co., Ltd. Any unauthorized use of Manual can be punished under applicable International or domestic law.